## Slide 1
Routing Made Simple
Noah Davids
Stratus Computer Inc.
Customer Assistance Center
1-800-828-8513
Noah_Davids@stratus.com
Stratagy 1997
Tucson, AZ

## Slide 2
Original Goals
review of a lot of protocols
  RIP, RIP-2, IGP, EGP, BGP, OSPF, IGRP
routing in
  TCP_OS, STCP, FTX & HP-UX

## Slide 3
Only have 1 hour I’m not that smart
Reality Check

## Slide 4
Overview
Pronunciation
Routing Basics
Protocols - RIP/RIP2
VOS - TCP_OS
FTX

## Slide 5
Pronunciation
British
  routing rhymes with toot
US
  routing, rhymes with out
  British pronunciation is also used
Australian
  routing rhymes with out
  British pronunciation is a “bad” word

## Slide 6
Routing Basics
What is it
  routing is the act of moving packets from a source network to a destination network
  layer 3 of the ISO stack
When do we need it
  whenever the destination system has an IP address with a different (sub)net than the sending address

## Slide 7
Routing Basics
What is a router
  route calculation
    given an incoming packet interpret the layer 3 address and select a route
  frame forwarding
    forward frames based on route calculation
    or selectively don’t forward frames
      unlimited broadcasts not forwarded
      local subnet traffic not forwarded
      can act as firewall to filter certain types of packets or packets from/to selected destinations or ports

## Slide 8
Routing Basics
Layer 3 switching - new buzz word
  really just a faster router
    the term router no longer in vogue
    rely on proprietary protocols to route packets faster (at layer 2 speeds)
    Ipsilon Networks
      flows technology
        recognizes long lived connections (10+ packets)
        sets up a virtual circuit to route them

## Slide 9
Routing Basics
What is a router (newfangled)
  Cisco
    tag switching
      proposed to Internet Engineering Task Force as a standard
  Bay Networks
    Adaptive Networking
  3Com
    Fast IP

## Slide 10
Routing Basics
What is a router (newfangled)
  Cabletron
    SecureFast
These protocols are not compatible with each other

## Slide 11
Routing Basics Selecting a Route (OS independent)
host route
  route to specific host
network route
  route to hosts network
default route
  specified default route if there is no host or network route that matches

## Slide 12
Routing Basics
Selecting a Route
  destination IP address not local
  routing table searched for route
  router identified
  packet created
    addressed to router at data link level
    addressed to destination at network layer

## Slide 13
Routing Protocols
Distance Vector
  router sends to all neighboring routers the distance (number of hops) to target networks
  neighbors add 1 to the hop count and add routes to their own tables if they don’t already have a route with a lower count
  hop count > some defined value implies the network is unreachable

## Slide 14
Routing Protocols
Distance Vector
  works well when routes are relatively static
  when routes change (routers and links going up and down) can take a long time to “converge”
    temporary loops caused by different routers having different routing tables cause packets to be lost
    long time can be up to 10 minutes
  lots of broadcasts
    too many hosts will generate broadcast storms

## Slide 15
Routing Protocols
Distance Vector
  Routing Information Protocol (RIP)
  Inter-Gateway Routing Protocol (IGRP)
    Cisco proprietary
  Gateway-to-Gateway Protocol (GGP)
  External Gateway Protocol (EGP)
  Hello
  Gated

## Slide 16
Routing Protocols
Link State
  each router maintains a copy of the entire network topology
  determines the shortest path to the target network
  multiple metrics can be associated with each link
    bandwidth, latency, cost,...

## Slide 17
Routing Protocols
Link State
  routers forward
    status changes of directly connected links
    status change messages from other routers that it receives
  works well with complex dynamic networks
  processing requirements larger than distance vector

## Slide 18
Routing Protocols
Link State
  Open Shortest Path First (OSPF)
  End System to Intermediate System (ES-IS)
  Intermediate System to Intermediate System (IS-IS)

## Slide 19
Routing Protocols ICMP
Internet Control Message Protocol (ICMP)
  not a routing protocol
  used between router and host system to correct host systems routing table
  redirect message type

## Slide 20
Routing Protocols RIP
RFC 1058 (1988)
  each router broadcasts all known networks every 30 seconds
    UDP messages to port 520
  receiving router adds routes to its routing table
    only if it doesn’t have a route with a lower hop count
    adds 1 to the hop count

## Slide 21
Routing Protocols RIP
  if route not mentioned in 180 seconds marked as unreachable
  if route not mentioned in 300 seconds discarded from table
  maximum number of hops is 15
    count of 16 means unreachable

## Slide 22
Routing Protocols RIP
Advantages
  easy to implement
  been around a long time
Disadvantages
  limited to 15 hops
  slow to converge
    prone to looping during convergence
  does not scale well into large networks

## Slide 23
Routing Protocols RIP version 2
Adds
  subnet mask
  authentication

## Slide 24
VOS - TCP_OS
protocols supported
management
interface selection

## Slide 25
VOS - TCP_OS protocols supported
static routing
dynamic changes via ICMP redirect
no “routing” protocols

## Slide 26
VOS - TCP_OS management routing table
netstat command
  netstat -nr
    displays the routing table
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 13256 #e4.20.13
default 134.111.44.240 UG 1 185574 #e4.20.12
10 134.111.44.196 UG 0 0 #e4.20.12
172.31 172.31.1.1 U 0 159 #e4.20.13
134.111.44 134.111.44.78 U 0 4003 #e4.20.12

## Slide 27
VOS - TCP_OS management netstat -nr
Destination
  host or network that is the destination of this route
    without the -n destination will be resolved to a host or network name if possible
Gateway
  packets for the destination are sent to this router
    without the -n gateway will be resolved to a host name

## Slide 28
VOS - TCP_OS management netstat -nr
Flags
  U route is up
  H this is a host route
  G packets are addressed to a gateway
  D dynamically created route (via ICMP)
  M dynamically modified route (via ICMP)

## Slide 29
VOS - TCP_OS management netstat -nr - example
Refs
  number of current users
Use
  number of times a packet was sent on this route
Interface
  interface to use

## Slide 30
VOS - TCP_OS management adding/deleting/flushing static routes
route command - to add/delete static routes
  route add [host|net] destination gateway metric
    destination may be IP address or name or the keyword default
    gateway may be IP address or name
    metric can just be 1
  route delete [host|net] destination gateway
  route -flush [-numeric]
    flushes all routes except local network routes

## Slide 31
VOS - TCP_OS management adding/deleting static routes examples
route add net 10.0.0.0 134.111.44.196 1
add net 10.0.0.0: gateway 134.111.44.196
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 13256 #e4.20.13
default 134.111.44.240 UG 1 185574 #e4.20.12
10 134.111.44.196 UG 0 0 #e4.20.12
172.31 172.31.1.1 U 0 159 #e4.20.13
134.111.44 134.111.44.78 U 0 4003 #e4.20.12
route delete net 10.0.0.0 134.111.44.196
delete net 10.0.0.0: gateway 134.111.44.196

## Slide 32
VOS - TCP_OS management flushing static routes examples
route add net 10.0.0.0 134.111.44.196 1
add net 10.0.0.0: gateway 134.111.44.196
route -flush -numeric
Flushing routing tables:
default 134.111.44.240 done
10 134.111.44.196 done
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 13256 #e4.20.13
172.31 172.31.1.1 U 0 159 #e4.20.13
134.111.44 134.111.44.78 U 0 4003 #e4.20.12

## Slide 33
VOS - TCP_OS management routing statistics
netstat command
  netstat -rs
    displays routing statistics
netstat -rs -display_zeros
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
5 uses of a wildcard route

## Slide 34
VOS - TCP_OS management netstat -rs
bad routing redirects
  received a redirect message
    telling us to use a router not a local subnet
    from a router that is not the router we used for the indicated destination
    telling us that we are the correct router for the destination

## Slide 35
VOS - TCP_OS management netstat -rs
dynamically created routes
  number of dynamically created (new) routes
new gateways due to redirects
  number of times where the gateway to the destination was dynamically changed

## Slide 36
VOS - TCP_OS management netstat -rs
destinations found unreachable
  number of times there was no LOCAL route to the destination.
    This can only happen if there is no default route. If one of the routers on the path sends an unreachable message it will not be recorded here

## Slide 37
VOS - TCP_OS management netstat -rs
uses of a wild card route
  this is the default route

## Slide 38
VOS - TCP_OS management routing statistics examples
netstat -rs
routing:
5 uses of a wildcard route
netstat -rs -display_zeros
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
5 uses of a wildcard route

## Slide 39
VOS - TCP_OS management dynamic routes examples
ping 134.111.45.12 1
PING 134.111.45.12: 64 bytes (56 data)
----134.111.45.12 PING Statistics----
1 packets transmitted, 0 packets received, 100% packet loss
netstat -rs -display_zeros
routing:
0 bad routing redirects
1 dynamically created route
0 new gateways due to redirects
0 destinations found unreachable
7 uses of a wildcard route

## Slide 40
VOS - TCP_OS management dynamic routes examples
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 0 #e4.20.13
134.111.45.12 134.111.44.250 UGHD 0 0 #e4.20.12
default 134.111.44.240 UG 0 10365 #e4.20.12
172.31 172.31.1.123 U 0 10 #e4.22.9
172.31 172.31.1.1 U 0 0 #e4.20.13

## Slide 41
VOS - TCP_OS management new gateways examples
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
134.111.45.12 134.111.44.240 UGH 0 0 #e4.20.12
ping 134.111.45.12 1
PING 134.111.45.12: 64 bytes (56 data)
----134.111.45.12 PING Statistics----
1 packets transmitted, 0 packets received, 100% packet loss

## Slide 42
VOS - TCP_OS management new gateways examples
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
134.111.45.12 134.111.44.250 UGHM 1 1 #e4.20.12
netstat -rs -display_zeros
routing:
0 bad routing redirects
1 dynamically created route
1 new gateway due to redirects
0 destinations found unreachable
7 uses of a wildcard route

## Slide 43
VOS - TCP_OS management unreachable networks examples
ping 12.1.1.1
PING 12.1.1.1: 64 bytes (56 data)
sendto: Network is unreachable.
ping: wrote 12.1.1.1 64 chars, ret=-1
sendto: Network is unreachable.
netstat -rs -display_zeros
routing:
0 bad routing redirects
1 dynamically created route
1 new gateway due to redirects
2 destinations found unreachable
9 uses of a wildcard route

## Slide 44
VOS - TCP_OS management wildcard routes
netstat -rs -display_zeros
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
32 uses of a wildcard route
ready 15:32:31
ping 198.115.44.38
PING 198.115.44.38: 64 bytes (56 data)
64 bytes from 198.115.44.38: icmp_seq=0. time=8. ms
...
64 bytes from 198.115.44.38: icmp_seq=19. time=7. ms
----198.115.44.38 PING Statistics----
20 packets transmitted, 20 packets received, 0% packet loss
round-trip (ms) min/avg/max = 7/8/14

## Slide 45
VOS - TCP_OS management wildcard routes
netstat -rs -display_zeros
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
33 uses of a wildcard route

## Slide 46
VOS - TCP_OS management wildcard routes
ping 198.115.44.38 2
PING 198.115.44.38: 64 bytes (56 data)
64 bytes from 198.115.44.38: icmp_seq=0. time=10. ms
64 bytes from 198.115.44.38: icmp_seq=1. time=8. ms
----198.115.44.38 PING Statistics----
2 packets transmitted, 2 packets received, 0% packet loss
round-trip (ms) min/avg/max = 8/9/10
ready 15:36:15
netstat -rs -display_zeros
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
34 uses of a wildcard route

## Slide 47
VOS - TCP_OS management IP forwarding
If IP forwarding is on
  packets received with the correct MAC address but the wrong IP address will be forwarded to an interface that can reach the indicated IP destination
  IP forwarding controlled by the variable tcpos_ipforwarding$
    value of 1 allows forwarding
    value of 0 stops forwarding

## Slide 48
VOS - TCP_OS management IP forwarding
if subnet mask doesn’t match rest of network
  IP broadcast address interpreted as a unicast address
    if module’s subnet mask is more restrictive we will forward packet - possibly to default router
    if module’s subnet mask is less restrictive we will interpret the IP address as being on the local subnet and try to forward it. Issuing an ARP first.

## Slide 49
VOS - TCP_OS management IP forwarding
IP statistics will indicate if we are forwarding packets or not.
We do not make a very good router

## Slide 50
VOS - TCP_OS management IP forwarding example
displaying value of tcpos_ipforwarding$
as: display tcpos_ipforwarding$
4C9198F0 0 00000001 |.... |
changing the value of tcpos_ipforwarding$
as: set_longword tcpos_ipforwarding$ 0 -check 1
addr from to
4C9198F0 00000001 00000000
as: set_longword tcpos_ipforwarding$ 1 -check 0
addr from to
4C9198F0 00000000 00000001

## Slide 51
VOS - TCP_OS management IP forwarding example
netstat -statistics -display_zeros
ip:
this machine is configured as a host, it is not able to forward packets.
255 default ttl on ip/icmp datagrams
62410211 datagrams received (incl. errors)
0 datagrams with ip uni-cast address
0 datagrams with ip multicast address
134 datagrams with invalid ip address
2 datagrams with header/options/checksum/ttl errors
0 bad header checksums
2 size < minimum
0 data size < data length
0 header length < data size
0 data length < header length
0 datagrams with unknown protocol
1736 datagrams discarded (no errors and not waiting re-
assembly)
161423 datagrams forwarded
62204439 datagrams delivered

## Slide 52
VOS - TCP_OS management IP forwarding example
this machine is configured as a host, it is not able to forward packets
  ignore this see otp-611
  the only way to tell is forwarding is being done is to check the value of tcpos_ipforwarding$
    1 will forward
    0 will not forward

## Slide 53
VOS - TCP_OS management IP forwarding example
datagrams with invalid ip address
  packets received with an IP address that doesn’t match any interface on the system but does have a correct MAC address
    IP forwarding is not enabled and someone is using us as a router

## Slide 54
VOS - TCP_OS management IP forwarding example
datagrams discarded (no errors and not waiting re-assembly)
  will be incremented if ip forwarding is enabled but there is no route (implies no default route)
datagrams forwarded
  count of the packets forwarded or attempted to forward

## Slide 55
VOS - TCP_OS management traceroute
utility to trace the route taken by a “ping” packet through the network.
reports each router’s name and the time it takes to get to the router
NOT supported by TCP_OS

## Slide 56
VOS - TCP_OS interface selection
direct connect routes
  destinations on a local network
  use first defined interface in the routing table
    last defined (ifconfig -add_name) interface
via gateway routes
  destinations not on the local network
  use first defined entry in the interface table that is on the router’s network

## Slide 57
VOS - TCP_OS interface selection - example
ifconfig %phx_test#e4.20.13 172.31.1.1 -state up -netmask 255.255.0.0
%phx_test#e4.20.13: <UP,BROADCAST,NOTRAILERS,RUNNING>
172.31.1.1 netmask 0xffff0000 broadcast 172.31.255.255
ifconfig %phx_test#e4.22.9 172.31.1.123 -state up -netmask 255.255.0.0
%phx_test#e4.22.9: <UP,BROADCAST,NOTRAILERS,RUNNING>
172.31.1.123 netmask 0xffff0000 broadcast 172.31.255.255
netstat -ni
Ifc: "Device Name" Name: "Interface Name"
# Mtu Network Ipkts Ierrs Opkts Oerrs Coll Queue
Ifc: loopback Name: 127.0.0.1
1536 loopback 0 0 0 0 0 0
Ifc: #e4.20.13 Name: 172.31.1.1
0 1500 172.31 0 0 1 0 26447 0
Ifc: #e4.22.9 Name: 172.31.1.123
1 1500 172.31 0 0 1 0 0 0

## Slide 58
VOS - TCP_OS interface selection - example
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 0 #e4.20.13
172.31 172.31.1.123 U 0 0 #e4.22.9
172.31 172.31.1.1 U 0 0 #e4.20.13

## Slide 59
VOS - TCP_OS interface selection - example
route add 10.0.0.0 172.31.1.100 1
add net 10.0.0.0: gateway 172.31.1.100
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 0 #e4.20.13
10 172.31.1.100 UG 0 0 #e4.20.13
172.31 172.31.1.123 U 0 0 #e4.22.9
172.31 172.31.1.1 U 0 0 #e4.20.13

## Slide 60
VOS - TCP_OS interface selection direct connect route example
ping 172.31.1.101 5
PING 172.31.1.101: 64 bytes (56 data)
----172.31.1.101 PING Statistics----
5 packets transmitted, 0 packets received, 100% packet loss
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 0 #e4.20.13
10 172.31.1.100 UG 0 0 #e4.20.13
172.31 172.31.1.123 U 0 5 #e4.22.9
172.31 172.31.1.1 U 0 0 #e4.20.13

## Slide 61
VOS - TCP_OS interface selection via gateway route example
ping 10.1.1.1 6
PING 10.1.1.1: 64 bytes (56 data)
----10.1.1.1 PING Statistics----
6 packets transmitted, 0 packets received, 100% packet loss
netstat -nr
Routing tables
Destination Gateway Flags Refs Use Interface
127.0.0.1 127.0.0.1 UH 0 0 #e4.20.13
10 172.31.1.100 UG 0 6 #e4.20.13
172.31 172.31.1.123 U 0 5 #e4.22.9
172.31 172.31.1.1 U 0 0 #e4.20.13

## Slide 62
FTX
protocols supported
management
interface selection

## Slide 63
FTX protocols supported
static routing
dynamic changes via ICMP redirect
when running in.routed
  RIP
    version 1 only

## Slide 64
FTX - management routing table
netstat command
  netstat -nr
    displays routing table
hera# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
default 134.111.44.240 UG 0 0 enet/c20a12d0
10 10.3.3.3 U 4 26689451 fddi/c24a0d0
199.115.44 199.115.44.211 U 0 1 enet/c20a13d0
134.111.44 134.111.44.211 U 7 62355 enet/c20a12d0
172.31 172.31.1.2 U 0 106 enet/c20a11d0

## Slide 65
FTX management netstat -nr
Destination
  host or network that is the destination of this route
    without the -n destination will be resolved to a host or network name if possible
Gateway
  packets for the destination are sent to this router
    without the -n gateway will be resolved to a host name

## Slide 66
FTX management netstat -nr
Flags
  U route is up
  H this is a host route
  G packets are addressed to a gateway
  D dynamically created route (via ICMP)
Note no M flag

## Slide 67
FTX management netstat -nr - example
Refs
  number of current users
Use
  number of times a packet was sent on this route
Interface
  interface to use

## Slide 68
FTX - management adding & deleting static routes
route command - to add/delete static routes
  route add [host|net] destination gateway metric
    destination may be IP address or name or the keyword default
    gateway may be IP address or name
    metric can be just 1
  route delete [ host|net] destination gateway
  route -f [n]
    flushes all routes except local network routes

## Slide 69
FTX - management adding/deleting static routes examples
VOS example used IP address, this uses names but it could just have
easily been reversed.
Note that to use names the names must be resolvable. gateway name can
be in the host table or resolved via a DNS. The network name must be in
the networks table.

## Slide 70
FTX - management flushing static routes examples
hera# route -f
Flushing routing tables:
default cisco done
11 cisco done
hera# route -fn
Flushing routing tables:
default 134.111.44.240 done
11 134.111.44.240 done

## Slide 71
FTX - management routing statistics
netstat command
  netstat -rs
    displays routing statistics
    exactly the same as TCP_OS
netstat -rs
routing:
1 bad routing redirect
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
53 uses of a wildcard route

## Slide 72
FTX management netstat -rs
bad routing redirects
  received a redirect message
    telling us to use a router not a local subnet
    from a router that is not the router we used for the indicated destination
    telling us that we are the correct router for the destination

## Slide 73
FTX management netstat -rs
dynamically created routes
  number of dynamically created (new) routes
new gateways due to redirects
  number of times where the gateway to the destination was dynamically changed

## Slide 74
FTX management netstat -rs
destinations found unreachable
  number of times there was no LOCAL route to the destination.
    This can only happen if there is no default route. If one of the routers on the path sends an unreachable message it will not be recorded here

## Slide 75
FTX management netstat -rs
uses of a wild card route
  this is the default route

## Slide 76
FTX management routing statistics examples
hera# netstat -sr
routing:
1 bad routing redirect
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
53 uses of a wildcard route

## Slide 77
FTX - management dynamic routes example
hera# netstat -sr
routing:
1 bad routing redirect
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
53 uses of a wildcard route
hera# ping 134.111.45.12 1
ICMP Host redirect from gateway cisco (134.111.44.240)
to nb1 (134.111.44.250) for windowrock (134.111.45.12)
no answer from 134.111.45.12
If the ICMP redirect message comes back before the ping times out you will see it. If it doesn’t you won’t.

## Slide 78
FTX - management dynamic routes example
hera# netstat -sr
routing:
1 bad routing redirect
1 dynamically created route
0 new gateways due to redirects
0 destinations found unreachable
56 uses of a wildcard route
hera# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
134.111.45.12 134.111.44.250 UGHD 0 1 enet/c20a12d0
default 134.111.44.240 UG 0 1 enet/c20a12d0
134.111.44 134.111.44.211 U 7 62450 enet/c20a12d0

## Slide 79
FTX - management new gateways example
hera# route add 134.111.45.12 134.111.44.240 1
add host 134.111.45.12: gateway 134.111.44.240
hera# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
134.111.45.12 134.111.44.240 UGH 0 0 enet/c20a12d0
default 134.111.44.240 UG 0 1 enet/c20a12d0
10 10.3.3.3 U 3 26877409fddi/c24a0d0
199.115.44 199.115.44.211 U 0 1 enet/c20a13d0
134.111.44 134.111.44.211 U 7 62753 enet/c20a12d0
172.31 172.31.1.2 U 0 106 enet/c20a11d0

## Slide 80
FTX - management new gateways example
hera# ping 134.111.45.12 1
ICMP Host redirect from gateway cisco (134.111.44.240)
to nb1 (134.111.44.250) for windowrock (134.111.45.12)
no answer from 134.111.45.12
hera# netstat -rs
routing:
1 bad routing redirect
1 dynamically created route
1 new gateway due to redirects
0 destinations found unreachable
56 uses of a wildcard route

## Slide 81
FTX - management new gateways example
hera# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
134.111.45.12 134.111.44.250 UGH 0 3 enet/c20a12d0
default 134.111.44.240 UG 0 1 enet/c20a12d0
10 10.3.3.3 U 3 26895963 fddi/c24a0d0
199.115.44 199.115.44.211 U 0 1 enet/c20a13d0
134.111.44 134.111.44.211 U 7 62815 enet/c20a12d0
172.31 172.31.1.2 U 0 106 enet/c20a11d0
Note no M flag

## Slide 82
FTX - management unreachable networks examples
hera# netstat -rs
routing:
0 bad routing redirects
2 dynamically created routes
0 new gateways due to redirects
4 destinations found unreachable
25 uses of a wildcard route
hera# ping -s 12.1.1.1
PING 12.1.1.1: 56 data bytes
----12.1.1.1 PING Statistics----
33 packets transmitted, 0 packets received, 100% packet loss

## Slide 83
FTX - management unreachable networks examples
hera# netstat -rs
routing:
0 bad routing redirects
2 dynamically created routes
0 new gateways due to redirects
6 destinations found unreachable
25 uses of a wildcard route
hera# telnet 12.1.1.1
Trying 12.1.1.1 ...
telnet: connect: Network is unreachable
telnet> quit
hera# netstat -rs
routing:
...
10 destinations found unreachable
...

## Slide 84
FTX - management wildcard routes
# netstat -rs
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
36 uses of a wildcard route
# ping -s 134.111.44.50 64 4
PING 134.111.44.50: 64 data bytes
72 bytes from (134.111.44.50): icmp_seq=0. time=0. ms
...
72 bytes from (134.111.44.50): icmp_seq=3. time=0. ms
----134.111.44.50 PING Statistics----
4 packets transmitted, 4 packets received, 0% packet loss
round-trip (ms) min/avg/max = 0/0/0

## Slide 85
FTX - management wildcard routes
# netstat -rs
routing:
0 bad routing redirects
0 dynamically created routes
0 new gateways due to redirects
0 destinations found unreachable
41 uses of a wildcard route

## Slide 86
FTX - management ipforwarding
If IP forwarding is on
  packets received with the correct MAC address but the wrong IP address will be forwarded to an interface that can reach the indicated IP destination
  IP forwarding controlled by the variable ipforwarding
    value of 1 allows forwarding
    value of 0 stops forwarding

## Slide 87
FTX - management ipforwarding
default fault is off
  set in /etc/conf/pack.d/ip/space.c
can change value via crash

## Slide 88
FTX - management ipforwarding
if subnet mask doesn’t match rest of network
  IP broadcast address interpreted as a unicast address
    if module’s subnet mask is more restrictive we will forward packet - possibly to default router
    if module’s subnet mask is less restrictive we will interpret the IP address as being on the local subnet and try to forward it. Issuing an ARP first.

## Slide 89
FTX - management ipforwarding
IP statistics will indicate if we are forwarding packets or not.
We do not make a very good router

## Slide 90
FTX - management ipforwarding example
displaying the value of ipforwarding
C0> od ipforwarding
04380370: 00000000 .…
setting the ipforwarding value to allow forwarding
C0> w4 ipforwarding 1
setting the ipforwarding value to prevent forwarding
C0> w4 ipforwarding 0

## Slide 91
FTX - management ipforwarding example
netstat -s
ip:
75896433 total packets received
0 bad header checksums
0 with size smaller than minimum
0 with data size < data length
0 with header length < data size
0 with data length < header length
9444 fragments received
0 fragments dropped (dup or out of space)
0 fragments dropped after timeout
16 packets forwarded
459117 packets not forwardable
0 redirects sent

## Slide 92
FTX - management ipforwarding example
packets forwarded
  count of the packets forwarded
packets not forwardable
  count of packets not forwardable
    no route
    ipforwarding set to 0

## Slide 93
FTX management routed
implements the RIP v1 protocol
when used, typically started in the /etc/rc2.d/S69inetinit script

## Slide 94
FTX management routed
usr/sbin/in.routed
  -q
    quiet mode, listens but does not broadcast routing tables
  -s
    forces the broadcast of routing tables
  -v PATH
    records changes to routing tables in file PATH
  -t
    records more info to tracing PATH or user_output
    program does not detach from controlling terminal

## Slide 95
FTX management routed
routed issues
  no way to tell from looking at netstat output that routing table has been updated via RIP messages
    routing table flags don’t show D flag
    dynamically created routes statistic not incremented

## Slide 96
FTX management routed
routed keeps a copy of the routing table, don’t change the routing table with the route command once routed is started
  use /etc/gateways to set initial routes

## Slide 97
FTX management /etc/gateways file
Contains a list of local and remote gateways
  gateways on routes marked passive or external are considered remote
  local gateways are expected to send RIP updates
    failure to do so will cause the associated routes to be removed

## Slide 98
FTX management /etc/gateways file
{ net|host } net_or_hostaddr gateway gateway_addr metric metric_value [ passive |external ]
  { net|host }
    Key words indicating type of route
  net_or_hostaddr
    address of the destination network or host. This can be a symbolic name located in /etc/networks or /etc/hosts or an internet address specified in dot notation.

## Slide 99
FTX management /etc/gateways file
  gateway
    required key word.
  gateway_addr
    address of the gateway to which messages should be forwarded.
  metric
    required key word.
  metric_value
    A metric value for hop count to the destination

## Slide 100
FTX management /etc/gateways file
  passive
    optional key word indicating that updates cannot be received for the entry and that the entry should not be aged for subsequent removal
      routes are added to routing table but not broadcast in RIP packets
      RIP updates are not expected from gateways marked passive

## Slide 101
FTX management /etc/gateways file
  external
    optional key word indicating that the entry is managed by a routing protocol other than rip
      routes NOT added to the routing table by routed
        assumes some other mechanism
      routes kept track of by routed so they are are not overwritten by RIP entries
      RIP updates are not expected from gateways marked external

## Slide 102
FTX management routed and /etc/gateways file
parsing of the /etc/gateways file has some bugs
  f2net-1434
    only external, passive and the default route can be specified

## Slide 103
FTX management routed and /etc/gateways file
# cat gateways
net 0.0.0.0 gateway 10.1.1.100 metric 1
net 12.0.0.0 gateway 10.1.1.112 metric 1 xxx
net 13.0.0.0 gateway 10.1.1.113 metric 1 passive
net 14.0.0.0 gateway 10.1.1.114 metric 1 external
# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 7 0 lo0
default 10.1.1.100 UG 0 0 enet/c10a13d0
10.1.1 10.1.1.10 U 1 3181 enet/c10a13d0
198.115.44 198.115.44.191 U 13 2600 enet/c4a5d0
13 10.1.1.113 UG 0 0 enet/c10a13d0

## Slide 104
FTX management routed and /etc/gateways file
Note that there is no route to network 12 but you need the entry to correctly add the first passive route
  Note the XXX after the metric - needed for correct parsing
adding another non-passive, non-external route will change the default route
  rely on RIP updates to add local routes

## Slide 105
FTX management routed log
Log entries created from defined interfaces and entries in the gateways file
# cat /tmp/route*
Sep 5 09:40:43 ADD dst 0.0.0.0 via 10.1.1.100 metric 1 state CHANGED
Sep 5 09:40:43 ADD dst 14.0.0.0 via 10.1.1.114 metric 1 state PASSIVE|CHANGED|EXTERNAL
Sep 5 09:40:43 ADD dst 198.115.44.0 via 198.115.44.191 metric 0 state INTERFACE|CHANGED UP
Sep 5 09:40:43 ADD dst 95.0.0.0 via 95.1.1.6 metric 0 state INTERFACE|CHANGEDUP
Sep 5 09:40:43 ADD dst 172.31.0.0 via 172.31.1.3 metric 0 state INTERFACE|CHANGED UP
Sep 5 09:40:43 ADD dst 10.0.0.0 via 10.1.1.10 metric 0 state PASSIVE|INTERFACE|CHANGED|INTERNAL|SUBNET UP

## Slide 106
FTX management routed log
Entry deleted because no RIP updates from local router
Sep 5 09:43:13 DELETE dst 0.0.0.0 via 10.1.1.100 metric 1 state 0

## Slide 107
FTX management routed log
Entries added/changed/deleted based on RIP updates from local router
Sep 5 09:47:27 ADD dst 198.115.51.0 via 198.115.44.1 metric 5 state CHANGED
Sep 5 09:47:32 ADD dst 198.115.55.0 via 198.115.44.1 metric 3 state CHANGED
Sep 5 09:47:32 ADD dst 192.92.20.0 via 198.115.44.1 metric 5 state CHANGED
Sep 5 09:48:42 CHANGE FROM dst 0.0.0.0 via 10.1.1.100 metric 1 state 0
Sep 5 09:48:42 CHANGE TO dst 0.0.0.0 via 198.115.44.1 metric 1 state CHANGED
Sep 5 09:51:20 DELETE dst 198.115.25.0 via 198.115.44.1 metric 5 state 0

## Slide 108
FTX management dynamic or static routes?
Dynamic full participation (sending RIP packets)
  module acting as a router in a dynamic network
    not just to a few other local hosts
Dynamic quiet mode
  local network has several routers which can back each other up
    gateways to specific networks may change dynamically

## Slide 109
FTX management dynamic or static routes?
Static
  local network has only 1 router or multiple routers which cannot back each other up
    gateways cannot change dynamically

## Slide 110
FTX - management traceroute
utility to trace the route taken by a “ping” packet through the network.
reports each router’s name and the time it takes to get to the router
NOT supported by FTX

## Slide 111
FTX interface selection
direct connect routes
  destinations on a local network
  use first defined interface in the routing table
    last defined interface
via gateway routes
  destinations not on the local network
  use first defined entry in the interface table that is on the router’s network
Notes: same as VOS

## Slide 112
FTX interface selection - examples
erebus% tail /etc/enet_config
enet/c4a5d0 198.115.44.191 255.255.255.0 -
enet/c5a5d0 95.1.1.6 - -
enet/c6a5d0 172.31.1.90 - -
enet/c7a5d0 172.31.1.91 - -
enet/c10a13d0 10.1.1.10 255.255.255.0 -
erebus% netstat -ni
Name Mtu Network Address Ipkts Ierrs Opkts Oerrs Collis
enet/c10a13d0 1500 10.1.1 10.1.1.10 0 0 7 0 0
lo0 2048 127 127.0.0.1 0 0 0 0 0
enet/c5a5d0 1500 95 95.1.1.6 0 0 0 0 0
enet/c4a5d0 1500 198.115.44 198.115.44.1 77 0 25 0 0
enet/c7a5d0 1500 172.31 172.31.1.91 0 0 0 0 0
enet/c6a5d0 1500 172.31 172.31.1.90 0 0 0 0 0

## Slide 113
FTX interface selection - examples
# route add 11.0.0.0 172.31.1.1 1
add net 11.0.0.0: gateway 172.31.1.1
# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
default 198.115.44.1 UG 1 162 enet/c4a5d0
10.1.1 10.1.1.10 U 0 0 enet/c10a13d0
11 172.31.1.1 UG 0 0 enet/c6a5d0
198.115.44 198.115.44.191 U 0 0 enet/c4a5d0
172.31 172.31.1.91 U 0 0 enet/c7a5d0
172.31 172.31.1.90 U 0 0 enet/c6a5d0
95 95.1.1.6 U 0 0 enet/c5a5d0

## Slide 114
FTX interface selection - examples
# ping 172.31.1.92 1
no answer from 172.31.1.92
# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
default 198.115.44.1 UG 1 188 enet/c4a5d0
10.1.1 10.1.1.10 U 0 0 enet/c10a13d0
11 172.31.1.1 UG 0 0 enet/c6a5d0
198.115.44 198.115.44.191 U 0 0 enet/c4a5d0
172.31 172.31.1.91 U 0 2 enet/c7a5d0
172.31 172.31.1.90 U 0 0 enet/c6a5d0
95 95.1.1.6 U 0 0 enet/c5a5d0

## Slide 115
FTX interface selection - examples
# ping 11.1.1.1 1
no answer from 11.1.1.1
# netstat -nr
Routing tables
Destination Gateway Flags Refcnt Use Interface
127.0.0.1 127.0.0.1 UH 0 0 lo0
default 198.115.44.1 UG 1 262 enet/c4a5d0
10.1.1 10.1.1.10 U 0 0 enet/c10a13d0
11 172.31.1.1 UG 0 2 enet/c6a5d0
198.115.44 198.115.44.191 U 0 0 enet/c4a5d0
172.31 172.31.1.91 U 0 2 enet/c7a5d0
172.31 172.31.1.90 U 0 0 enet/c6a5d0
95 95.1.1.6 U 0 0 enet/c5a5d0
127.0.0.1 127.0.0.1 UH 0 0 lo0 4608
10.3.3.0 10.3.3.9 U 1 39503 lan1 4352
10.3.3.0 10.3.3.7 U 0 0 lan0 4352
11 10.3.3.250 UG 0 1 lan0 4352