## Slide 1
Noah Davids
Stratus Computer Inc.
Customer Assistance Center
1-800-828-8513
John_Bilotti@Stratus.com

## Slide 2: Bill of Fare
What is it
documentation
how it works
network architecture
configuration
debugging

## Slide 3: What is dl_mux
Data link multiplexor
  introduced in VOS 13.2
  allows two network interfaces to be partnered to provide failover protection
    interfaces must be same hardware type
      K104, K450, K460, I104/K130
    1 interface goes broken
    network connection to 1 interface fails
      cable disconnect
      hub failure

## Slide 4: What dl_mux is NOT
Does not provide network load sharing across the two interfaces
  for K450 and K460 will attempt to make the active network interface on the standby SCSI controller
    network and disk activity on separate boards

## Slide 5: Documentation
VOS 13.2
  Appendix E of the VOS OS TCP/IP Administrator’s Guide (R223-04)
VOS 13.3
  Appendix A of the VOS OS TCP/IP Administrator’s Guide (R223-5)
VOS 14.1.0 (STCP release)
  VOS Data-Link Multiplexer Administrator’s Guide (R425)

## Slide 6: How it works

## Slide 7: How it works
dl_mux picks 1 interface to be the active interface
  this interface is given the primary MAC address 00:00:A8:8v:wx:yz
  this interface is used to send all outgoing IP packets and receiving incoming IP packets
the standby interface is given the MAC address 00:00:A8:Av:wx:yz

## Slide 8: How it works
When dl_mux determines that the active interface is no longer connected to the network
  it swaps the MAC addresses of the active and standby interface cards
    this is completely transparent to other hosts with connections to the module

## Slide 9: How it works Generating a new MAC address
00:00:A8:8v:wx:yz
  On Continuum systems
    v index of dl_mux entry
    wx:yz lower 15 bits of system serial number
    ORed with 8000x

## Slide 10: How it works Generating a new MAC address
00:00:A8:8v:wx:yz
  On non-Continuum systems
    v index of dl_mux entry
    wx:yz 0ddsssssmmmmmmmm
      dd lower 2 bits of disk_pack UID
      sssss lower 5 bits of system number
      mmmmmmmm lower 8 bits of module number

## Slide 11: How it works How it determines that something is broken
if board breaks we failover immediately
if board reports that carrier was lost we failover immediately
  k450 reports carrier lost immediately
  k460 reports carrier lost only when it tries to send something
  k104 does not report carrier lost until 13.3.2u
    fix for gdl-95
    may take 10 seconds to recognize lost or reconnect

## Slide 12: How it works messages when active K104 loses carrier
16:27:12 GDL device id: 04/06 Carrier is lost.
16:27:12 giza_dl_control.c: 2937: gdl_disconnect_real: Giza error during close
of device 04/07, state 106 Code = 1
16:27:12 GDL disconnecting. GDL device id: 04/07 channel: 1000046
16:27:12 GDL disconnecting. GDL device id: 04/07 channel: 1000113
16:27:12 GDL disconnecting. GDL device id: 04/07 channel: 1000111
16:27:12 GDL disconnecting. GDL device id: 04/07 channel: 100010f
16:27:12 GDL disconnecting. GDL device id: 04/07 channel: 100010d
16:27:12 GDL flushing. GDL device id: 04/07 channel: 1000047 type: 0
16:27:12 GDL flushing. GDL device id: 04/07 channel: 1000046 type: 1
16:27:12 GDL is disconnected. GDL device id: 04/07
16:27:12 GDL gdl_entry 3 is now undefined
16:27:12 GDL is connected to device id 04/07

## Slide 13: How it works messages when standby K104 loses carrier
16:29:53 GDL device id: 04/06 Carrier is lost.

## Slide 14: How it works messages when standby K104 restores carrier
16:30:32 GDL device id: 04/06 Carrier is restored.
16:30:32 GDL closing. GDL device id: 04/06 channel: 100011b type: 1
16:30:32 GDL closing. GDL device id: 04/06 channel: 100011a type: 0
16:30:32 GDL closing. GDL device id: 04/06 channel: 1000119 type: 1
16:30:32 GDL closing. GDL device id: 04/06 channel: 1000118 type: 0
16:30:33 GDL flushing. GDL device id: 04/06 channel: 100003f type: 0
16:30:33 GDL flushing. GDL device id: 04/06 channel: 100003e type: 1
16:30:33 GDL is disconnected. GDL device id: 04/06
16:30:33 GDL gdl_entry 2 is now undefined
16:30:33 GDL is connected to device id 04/06

## Slide 15: How it works K460 carrier lost/restored messages
disconnect cable from active interface. It took about 10 seconds to recognize the carrier lose.
Its can be much faster if there are active connections sending data. Note no dlmux message
indicating a failover even though dlmux did switch the active interface.
12:58:44 bdl_io.c: 613: bdl_hsc_scan_sent_ques: K460 in slot 3 lost carrier
reconnect cable to interface. Again about 10 seconds to recognize this but with an active
connection its much faster.
13:00:59 bdl_io.c: 624: bdl_hsc_scan_sent_ques: K460 in slot 3 had carrier res
tored
after 60 to 90 seconds dlmux may decide to move the active network connection back to the
standby SCSI controller.
13:01:59 dlmux_timers.c: 605: dlmux_generate_failover: failing over adapter %p
hx_cac_j#enet.13.2 to adapter %phx_cac_j#enet.13.3

## Slide 16: How it works How it determines that something is broken
dl_mux periodically polls the two interfaces and their network connection
  poll timing controlled by dlmux_test_interval$
    default value is 30 seconds
    default poll time is 45 seconds
      I have no idea why there is an extra 15 seconds

## Slide 17: How it works How it determines that something is broken
if secondary does not receive poll frame from primary
  listen for broadcast frames
    board that is receiving broadcasts is assumed to be on the network
  if neither card sees broadcasts (or they both do)
    if we have sent a non-test frame out and we haven’t gotten any inbound frames switch anyway

## Slide 18: How it works sniffer trace showing test frame timing
SUMMARY Delta T Destination Source Summary
1 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
2 0.0012 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
3 44.9986 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
4 0.0010 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
5 45.0001 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
6 0.0009 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
7 44.9990 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
8 0.0003 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
9 45.0008 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
10 0.0001 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
11 44.9994 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
12 0.0002 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F
13 45.0007 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
14 0.0004 Strtus8186D7 StrtusA186D7 LLC R D=AE S=AE Invalid U-type F

## Slide 19: How it works Poll Frame - standby to active
DLC: ----- DLC Header -----
DLC: Destination = Station Strtus8186D7
DLC: Source = Station StrtusA186D7
DLC: 802.3 length = 24
LLC: ----- LLC Header -----
LLC: DSAP Address = AE, DSAP IG Bit = 01 (Group Address)
LLC: SSAP Address = AE, SSAP CR Bit = 01 (Response)
LLC: Unnumbered frame: Invalid U-type, FINAL
LLC:
LLC: ERROR: Data is not allowed for this format
DLC: Frame padding= 26 bytes
ADDR HEX ASCII
0000 00 00 A8 81 86 D7 00 00 A8 A1 86 D7 00 18 AF AF ................
0010 F7 31 32 39 2E 31 2E 30 00 00 00 00 00 01 00 00 .129.1.0........
0020 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0030 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................

## Slide 20: How it works Poll Frame - active to standby
DLC: ----- DLC Header -----
DLC: Destination = Station StrtusA186D7
DLC: Source = Station Strtus8186D7
DLC: 802.3 length = 24
LLC: ----- LLC Header -----
LLC: DSAP Address = AE, DSAP IG Bit = 01 (Group Address)
LLC: SSAP Address = AE, SSAP CR Bit = 01 (Response)
LLC: Unnumbered frame: Invalid U-type, FINAL
LLC:
LLC: ERROR: Data is not allowed for this format
DLC: Frame padding= 26 bytes
ADDR HEX ASCII
0000 00 00 A8 A1 86 D7 00 00 A8 81 86 D7 00 18 AF AF ................
0010 F7 31 32 39 2E 31 2E 30 00 E8 C6 73 2C 01 FF FF .129.1.0...s,...
0020 FF FF 02 08 02 08 00 E8 00 00 02 01 00 00 00 02 ................
0030 00 00 C6 73 0D 00 00 00 00 00 00 00 00 00 00 00 ...s............

## Slide 21: How it works Fast Poll when active/secondary lose communication
SUMMARY Delta T Destination Source Summary
10 0.0000 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
11 2.9997 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
12 3.0012 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
14 3.0008 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
16 3.0003 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F
23 32.9985 StrtusA186D7 Strtus8186D7 LLC R D=AE S=AE Invalid U-type F

## Slide 22: How it works messages when poll fails and dlmux forces K104 failover
16:55:12 dlmux_timers.c: 788: dlmux_generate_failover: failing over adapter %p
hx_cac_j#tcp1.6 to adapter %phx_cac_j#tcp1.7
16:55:12 GDL closing. GDL device id: 04/07 channel: 1000127 type: 1
16:55:12 GDL closing. GDL device id: 04/06 channel: 1000123 type: 1
16:55:12 GDL closing. GDL device id: 04/07 channel: 1000126 type: 0
16:55:12 GDL closing. GDL device id: 04/06 channel: 1000122 type: 0
16:55:12 GDL closing. GDL device id: 04/07 channel: 1000125 type: 1
16:55:12 GDL closing. GDL device id: 04/06 channel: 1000121 type: 1
16:55:12 GDL closing. GDL device id: 04/07 channel: 1000124 type: 0
16:55:12 GDL closing. GDL device id: 04/06 channel: 1000120 type: 0
16:55:12 GDL flushing. GDL device id: 04/07 channel: 1000047 type: 0
16:55:12 GDL flushing. GDL device id: 04/06 channel: 100003f type: 0
16:55:12 GDL flushing. GDL device id: 04/07 channel: 1000046 type: 1
16:55:12 GDL flushing. GDL device id: 04/06 channel: 100003e type: 1
16:55:12 GDL is disconnected. GDL device id: 04/07
16:55:12 GDL gdl_entry 3 is now undefined
16:55:12 GDL is disconnected. GDL device id: 04/06
16:55:12 GDL gdl_entry 2 is now undefined
16:55:12 GDL is connected to device id 04/07
16:55:12 GDL is connected to device id 04/06

## Slide 23: How it works messages when poll fails and dlmux forces K460 failover
16:06:03 dlmux_timers.c: 803: dlmux_generate_failover: failing over adapter %p
hx_cac_j#enet.13.3 to adapter %phx_cac_j#enet.13.2

## Slide 24: How it works Network architecture requirements
Both partners must
be wired to the same
subnet
They have the same IP address after all

## Slide 25: How it works Network architecture requirements
It is not required that each interface be connected to a separate hub
  recommended so that if the hub fails the network connection is not lost - but not required
It is required that the two interfaces have a communication path at the data link layer
  this is so that the test frames can get through

## Slide 26: How it works Network architecture requirements
Partnered K460 interfaces must both be configured with the same line speed and duplex setting
  recommend setting speed and duplex values in the parameters field
  leaving values out of parameters field will result in autosensing which may result in different values

## Slide 27: How it works Network architecture examples
simplest configuration
no special setup needed on hub/repeater
provides fault tolerance only for Stratus interfaces

## Slide 28: How it works Network architecture examples
no special setup needed on hub/repeater
provides fault tolerance only for Stratus interfaces

## Slide 29: How it works Network architecture examples
no special setup needed on hub/repeater
no special setup needed on switch
provides fault tolerance only for Stratus interfaces
note only 1 connection between hub and switch
adding switch allows full duplex operation and dedicated bandwidth for devices directly connected to switch

## Slide 30: How it works Network architecture examples
2 connections directly to switch
  spanning tree algorithm must be off or frames could be lost during switch
provides fault tolerance only for Stratus interfaces
using switch allows for full duplex operation and dedicated bandwidth
Notes: Spanning tree algorithm is turned off to avoid the learning and listening times on ports which have changed. Times can be 10 of seconds. During learning/listening time any frames transmitted are ignored and frames received for those ports are just dropped.
The reason that Stratus must have no other interfaces on any network or IP forwarding must be off:
If interfaces are on same network then a problem with subnet masks may cause forwarding
If interfaces are on a different network and no other host on switch network is on that other network you are OK - but if it is and it is also forwarding then you again can have a loop.

## Slide 31: How it works Network architecture examples
2 switches provides fault tolerance for switch
  spanning tree algorithm must be off or frames could be lost during DLMUX switch
  if switch fails other hosts connected to switch will lose connection
using switch allows for full duplex operation and dedicated bandwidth

## Slide 32: How it works Network architecture examples
Fully redundant network
no special setup needed on hub/repeater
no special setup needed on switches
  spanning tree algorithm must be on
Stratus interfaces can only run in half duplex mode
  if they are the only interfaces on the hub/repeater this will not be significant
Notes: You need the two repeaters in the loop so that you can leave the spanning tree algorithm on without being hit by the learning/listening times
Its left as an exercise for the listener to determine how to get both switches onto the network

## Slide 33: How it works possible gotcha’s
Note that the poll frame has an IEEE 802.3 format not an Ethernet V2 format
  this has caused problems with certain bridges which change the format of the frames that they send to a host based on the format of the last frame seen from the host
  except for these frames all frames must be Ethernet V2
  bridges must be configured NOT to learn frame type based on received frames

## Slide 34
Host A
Stratus
Host B
Host C
HUB/Switch 2
HUB/Switch 1
Physical Router 1
Physical Router 2
Logical Router 1
The Internet

## Slide 35: How it works possible gotcha’s
Frame filtering
  network hardware must be configured to allow these 802.3 frames through
  802.3 frames are invalid - network hardware must allow this

## Slide 36: How it works possible gotcha’s
Interfaces directly connected to switches
  address cache issues
    When dlmux switches the interface the switch will not know it until something is sent. Until then any traffic for the interface will be forwarded to the switch port now connected to the standby interface - so we will not see it

## Slide 37: How it works possible gotcha’s
Interfaces directly connected to switches
  spanning tree issues
    When switch recognizes that a host has moved (changed ports) it may go through a period of learning/listening to reconfigure its spanning tree. During this time no traffic is forwarded from or to the port
    dlmux_test_interval$ must be longer than this learning/listening period or we can get into a condition where dlmux is always switching
      you can also turn the spanning tree off on the switch if that is an option
Notes: Bill Northup mentioned in the presentation
Some switches can be configured to try to stop address spoofing by
shutting down a port where the address changes. The address of the
interfaces change when there is a failover so the switch may shut down the
ports

## Slide 38: Configuration module_start_up - notes
Load kernel program
Needed after the hardware drivers loaded and before any of the TCP stuff.
Needed even if no interfaces are configured with a partner
network interfaces will not function properly until dlmux driver is loaded

## Slide 39: Configuration module_start_up - example
load_kernel_program >system>tcp_os>bdl driver
load_kernel_program >system>tcp_os>gdl driver
load_kernel_program >system>tcp_os>dlmux driver
load_kernel_program >system>tcp_os>tcp driver
load_kernel_program >system>tcp_os>tcp_kll library
note that bdl, gdl and dlmux will move to >system>kernel_loadable_library in VOS 13.4

## Slide 40: Configuration devices.tin - notes
parameter data is enclosed in single quotes
-partner begins with a dash
partner device name includes the hash character
mistakes will fail with no warnings or error messages

## Slide 41: Configuration devices.tin - example
/ =name tcp1.6
=module_name m13
=device_type ioa_gdma
=slot 4
=firmware_type hal
=adapter_slot_no 6
=adapter_subchannel_no 0
=parameters '-partner #tcp1.7'
/ =name tcp1.7
=module_name m13
=device_type ioa_gdma
=slot 4
=firmware_type hal
=adapter_slot_no 7
=adapter_subchannel_no 0
=parameters '-partner #tcp1.6'

## Slide 42: Configuration partnering requirements
Only like devices can be partnered
Partnered K450s and K460s must be adjacent slots
Partnered K104s can be in any ioa slot

## Slide 43: Configuration ifconfig’ing the interface
Do an ‘ifconfig -addname’ of only 1 on the partners
  this becomes the “name” of the interface regardless of which partner is active and which is standby
Doing an ‘ifconfig -state down’ will bring down both interfaces
  removing the IP address from the network

## Slide 44: dlmux messages
05:28:28 dlmux_timers.c: 952: dlmux_generate_rsn_call: Device %swok3#hsc_enet.m
+1.4 not responding to DLMUX testing
Generated no more than once per day per adapter
Failure count >= 10
  count increated every time test message fails
  count decremented every time test message succeeds
    will not go below 0

## Slide 45: dlmux messages
13:01:59 dlmux_timers.c: 605: dlmux_generate_failover: failing over adapter %p
+hx_cac_j#enet.13.2 to adapter %phx_cac_j#enet.13.3
issued when dlmux changes the active interface because of a test message failure

## Slide 46: dlmux messages
17:03:55 dlmux_control.c: 711: dlmux_generate_failover: failing over adapter %
+phx_cac_j#enet.13.3 to adapter %phx_cac_j#enet.13.2
Issued when a manual failover is done via dlmux_admin command

## Slide 47: other messages
16:29:53 GDL device id: 04/06 Carrier is lost.
issued by gdl when it noticies that an interface has lost carrier
16:33:32 GDL device id: 04/06 Carrier is restored.
issued by gdl when it noticies that an interface regained carrier

## Slide 48: other messages
12:58:44 bdl_io.c: 613: bdl_hsc_scan_sent_ques: K460 in slot 3 lost carrier
issued by bdl_io when it noticies that an interface has lost carrier
13:00:59 bdl_io.c: 624: bdl_hsc_scan_sent_ques: K460 in slot 3 had carrier
+restored
issued by bdl_io when it noticies that an interface has carrier

## Slide 49: other messages
13:01:59 Cannot duplex slot 5 - enet state:7 partner state: 6
Will be seen during boot
  jmd-585, fixed in 13.3
may also be seen after a failover message
as long as dlmux shows both partners UP don’t worry

## Slide 50: other messages
16:06:04 Cannot pair slots 3 and 2 - enet ports not paired
SYSERR {52018013 Diagnostic_Utility.System}
16:06:04 Slot 3 enet state: 7 partner state: 6
SYSERR {52018013 Diagnostic_Utility.System}
16:06:04 Slots 2 and 3 are now running paired
SYSERR {52018013 Diagnostic_Utility.System}
Appears in syserr_log only (not console output) after a failover in 13.4 system

## Slide 51: Status Lights
Green Light
  boards (not necessarily disks) and ENET duplexed or boards duplexed and ENET not configured
Green and Yellow Lights
  boards not duplexed or ENET configured but not duplexed
early versions of dlmux may not do this
  13.3 does it right

## Slide 52: dlmux and OSL
OSL can failover to another logical link before DLMUX can switch to another physical network interface.
Whether OSL will failover to another logical link or the DLMUX will failover to another physical link depends on the timing of events.
  If OSL has sent some packets and TCP has received its ACKs and OSL is just waiting for the other host’s OSL to respond, then OSL will probably not failover.
  If TCP has not received an ACK then it will retransmit and this time be told that the carrier is down and DLMUX will failover.

## Slide 53: dlmux and OSL phase 1
initial connection request timer is 7 seconds
  not adjustable
once connection is established OSL expects a response within 100 seconds (by default)
  time controlled by the -response_timeout parameter of the open_stratalink_client

## Slide 54: dlmux and OSL phase 2
initial connection request timer is by default 7 seconds
  adjustable via the kernel parameter osl_connect_timeout$
once connection is established OSL expects a response within 70 seconds (by default)
  adjustable via the kernel parameters osl_xfer_time$ and osl_xfer_tries$

## Slide 55: dlmux and OSL phase 2
timeout is
  osl_xfer_time$ + (osl_xfer_time$ * osl_xfer_tries$)
  default values are:
    osl_xfer_time$ 10 seconds
    osl_xfer_tries$ 6

## Slide 56: Debugging dlmux_admin command
--------------------------------- dlmux_admin --------------------------------
device_name:
action: get_status
-partner:
actions: get_status, add_partner, delete_partner, failover
dlmux_admin #tcp1.6 get_status
Device Name: %phx_cac_j#tcp1.6
Adapter State: ACTIVE UP
Partner: %phx_cac_j#tcp1.7
Partner State: UP
dlmux_admin #tcp1.7 get_status
Device Name: %phx_cac_j#tcp1.7
Adapter State: UP
Partner: %phx_cac_j#tcp1.6
Partner State: ACTIVE UP

## Slide 57: Debugging manual failover to partner
To manually failover you must issue dlmux_admin using the standby interfaces name and the failover action
wrong
  dlmux_admin #enet.13.6 failover
  dlmux_admin: The requested operation is inconsistent with the current device state.
  ready 17:02:23
right
  dlmux_admin #enet.13.7 failover
  ready 17:02:38

## Slide 58: Debugging dump_dlmux_info
as: dump_dlmux_info
dlmux adapter entry @0xE4EC7384
name: %phx_cac_j#tcp1.8
device id: 0408FFFF
state: open
flags: rsvd asgnd
adapter_index: 0
client_index: 0
adapter_type: 55
mac_addr: 0000A88086D7
dvtep: C0BB23C0

## Slide 59: Debugging dump_dlmux_info
dlmux adapter entry @0xE4EC752C
name: %phx_cac_j#tcp1.6
device id: 0406FFFF
state: open
flags: testing rsvd asgnd
adapter_index: 2
client_index: 1
adapter_type: 55
mac_addr: 0000A88186D7
dvtep: C0BB20C0
dlmux adapter entry @0xE4EC7600
name: %phx_cac_j#tcp1.7
device id: 0407FFFF
state: test open
flags: partner testing rsvd asgnd
adapter_index: 3
client_index: 1
adapter_type: 55
mac_addr: 0000A8A186D7
dvtep: C0BB2240
Notes: Can match up patners via the client_index value - partners will have the same value.

## Slide 60: Debugging dump_dlmux_info flags
partner
  this device is the "secondary" device
testing
  the dlmux is currently testing this device
dev_reserved (rsvd)
  reserve_device has been called by the dlmux
dev_assigned (asgnd)
  assign_device has been called by the dlmux
user_selected
  the user has issued a 'failover' for this device using the dlmux_admin command

## Slide 61: Debugging “netstat -detail” - notes
netstat -detail #INTERFACE will provide details only for active interface
  statistics are reset after a failover
no way to get statistics for standby K104 interface
dump_bdl_entry can be used to display statistics for standby K450 and K460

## Slide 62: Debugging “netstat -detail” - example
netstat -detail #tcp1.6
Interface Summary:
Interface Number: 1 Device Name: #tcp1.6 IP Address: 10.1.1.1
Maximum Transmit Unit (MTU): 1500
Line Speed : 10000000
Administrative Status : UP
Operational Status : UP
INPUT OUTPUT
----- ------
Packets : 82 34
Octets : 5381 2236
Errors : 0 0
Discards : 28 0
Ucast Packets : 77
NUcast Packets : 5
Out Qlen : 0
Unknown Protocols : 28

## Slide 63: Debugging “netstat -detail” - example
MAC Statistics:
MAC Type : CSMA/CD MAC Address: 00:00:a8:81:86:d7
Received frames : 77037
Received multicast and broadcast frames : 73
Received octets : 5245089
Transmitted frames : 423809
Transmitted octets : 41302544
LAN Chipset re-initialized : 1
SQE error : 0
Transmit ring full : 0
Transmit frame discarded, late collisions: 0
Transmit frame was deferred : 699
Transmit frame after a single retry : 86
Transmit frame after multiple retry : 63
Transmit frame discarded, excessive retry: 0

## Slide 64: Debugging “netstat -detail” - example
Receive frame discarded, lack of buffers : 0
Receive frame discarded, improper framing: 0
Receive frame discarded, an overflow : 0
Receive frame discarded, bad CRC : 0
Receive frame discarded, bad address : 0
Receive frame discarded, congestion : 0
MAC Summary:
Transmitted frames : 423809
Transmitted octets : 41302544
Retransmitted frames : 848
Received frames : 77110
Received octets : 5245089
Received invalid frames : 0

## Slide 65: Debugging “dump_gdl_entry” - example
as: dump_gdl_entry 2
----GDL ADAPTER ENTRY----
Entry : 2
State : ADAPTER_CONN (200)
Flags: COME_UP_RUNNING
device_id : 0406FFFF
iop_slot : 4
ioa_slot : 0006
board_type : K104 (67)
mac_type : ETHERNET_CSMACD (6)
mac_addr : 00:00:a8:81:86:d7
state_change_callback : dlmux_control+3E80, line 2564 (E4EC0E80)
free_buf_call : bufman+1378, line 1367 (E4E07738)
get_buf_call : tcp_dlm_utils+488, line 162 (E4E1D308)

## Slide 66: Debugging “dump_gdl_entry” - example
put_buf_up_call : dlmux_io+3E0, line 363 (E4EC2DE0)
put_attr_up_call : dlmux_control+39C8, line 2270 (E4EC09C8)
attr_descp : 00000000
attr_bufp : 00000000
attr_len : 0
----ADAPTER ERROR STATISTICS----
send_data_callback errors : 0
recv_data_callback errors : 0
send_ctrl_callback errors : 0
recv_ctrl_callback errors : 0
send_rpc_callback errors : 0
recv_rpc_callback errors : 0
----GIZA CHANS TO/FROM ADAPTER----
Send_data_chan : 0100010E
Recv_data_chan : 0100010C

## Slide 67: Debugging “dump_gdl_entry” - example
Send_rpc_chan : 01000112
recv_rpc_chan : 01000110
Send_ctrl_chan : 0100003E
recv_ctrl_chan : 0100003F
----BUFFER HANDLES----
free handle ptr : C0C8F000
free handle cnt : 61
xmit handles pending : 0
recv handles pending : 192
----CONMAN REQUESTS----
free con bufp : C0C8A300
free ctrl bufp : C0C8B900

## Slide 68: Debugging “dump_bdl_entry” - example
as: dump_bdl_entry 4
-------------BDL ADAPTER ENTRY------------
Entry : 4
adapter_state : BDL_ADAPTER_CONN
bio_device_id : 0205FFFF
config_word : 34
board_type : HSC (52)
mac_addr: : 0000A88286D7
state_change_callback : dlmux_control+3AD8, line 2318 (E4EC0AD8)
free_buf_call : bufman+1378, line 1367 (E4E07738)
get_buf_call : tcp_dlm_utils+488, line 162 (E4E1D308)
put_buf_up_call : dlmux_io+288, line 286 (E4EC2C88)
put_attr_up_call : dlmux_control+38B8, line 2222 (E4EC08B8)

## Slide 69: Debugging “dump_bdl_entry” - example
---------ADAPTER ERROR STATISTICS----------
cnt_frame_err : 0
cnt_short_frame : 0
cnt_long_frame : 0
cnt_lost_carrier : 0
cnt_no_carrier : 0
cnt_dma_under : 0
cnt_dma_over : 0
cnt_no_eop : 0
cnt_no_bde : 0
cnt_max_xmit : 0
cnt_no_buf : 0
cnt_lost_cts : 0
-------------------------------------------
Notes: Note sure if we can trust these error numbers in 13.4 - on going issue

## Slide 70: Debugging “dump_bdl_entry” - example
------------BDL Buffer Entry Queue----------
xmit_bh_pend_que : 1
xmit_bh_sent_queue : 1
recv_bh_sent_queue : C0C3B044
---------------BDL End Buffer Queue--------
-----------------BDL BIO Driver Queues-----
bde_free_queue : C15E3580
bde_abort_queue : C15D32C0
xmit bde sent queue : 1
recv_bde_sent_queue : 00000001
xfer_bde_sent_queue : 1
ctrl_bde_sent_queue : C15E5000
------------------ End BIO Queue-----------

## Slide 71: Debugging When all else fails
Make sure that card and hub are configured the same way
If running at 100 mbps try 10
  cat 5 cable, connectors, or installation may be substandard
If running full duplex try half duplex
  if its not a K460 it MUST be half duplex
If running on a K104 make sure transceiver has SQE turned on

## Slide 72: Debugging When all else fails
Delete the standby partner
  dlmux_admin -delete_partner
  Deal with only 1 interface at a time

## Slide 73: Debugging When at the end of your rope
Call the CAC