## Slide 1
Noah Davids
Stratus Computer Inc.
Customer Assistance Center
1-800-828-8513
Noah_Davids@Stratus.com

## Slide 2: Bill of Fare
what is it
documentation
how it works
network architecture
configuration
debugging

## Slide 3: what is RNI
Redundant Network Interface (RNI)
  introduced in FTX 2.3
  allows multiple network interfaces to be partnered to provide failover protection
    interfaces can be different types
      K104, K450, K460, U510, U512, U513, I104/K130, U530
    1 interface goes broken
    network connection to 1 interface fails
      cable disconnect
      hub failure
  can provide network load sharing

## Slide 4: what is RNI
Separately purchased software
RNI version dependent on FTX version
  FTX RNI
  2.3 1.0, 1.1
  3.0.1 1.1
  3.2 1.3
  3.3 1.4
  3.4 1.5

## Slide 5: documentation
FTX Redundant Network Interface (RNI) Release Notes and Installation Instructions
  RNI Document
  1.0 R252X-00
  1.1 R470X-00
  1.3 R470X-01
  1.4 R470X-02

## Slide 6: documentation
FTX Redundant Network Interface (RNI) Administrator’s Guide
  RNI Document
  1.0 R252X-00
  1.1 R471X-00
  1.4 R471X-01

## Slide 7: how it works

## Slide 8: how it works
RNI driver sits between IP and the hardware
Quality of Service (QoS) type controls how RNI transmits and receives packets
By default the first interface in the RNI group is used to send and receive frames

## Slide 9: Quality of Service (QoS)
Transmit
  online
    default mode
    packets are transmitted from only 1 interface (the same as the receive interface) until a failure is detected.
    Once a failure is detected the active interface is switched to the next interface in the group definition

## Slide 10: Quality of Service (QoS)
Transmit
  broadcast
    all packets are sent out each interface in the group
    receiving node will receive duplicate packets
  roundrobin
    each interface in the group will take turns sending a packet
    its possible that the packets will arrive out of order, even if interfaces are on the same data link layer
Notes: Assume two interfaces on the same data link layer. Interface 1 gets packet 1 to send, trys to send it and gets defered. Interface 2 gets packet 2 to send, trys to send it and gets deferred. When the data link layer is free both try to send and get a collision. Both back off a random amount. Its possible that interface 2 backs off less and therefore sends packet 2 before interface 1 sends packet 1.

## Slide 11: Quality of Service (QoS)
Receive
  online
    default mode
    packets are received from only 1 interface (the same as the transmit interface) until a failure is detected.
    Once a failure is detected the active interface is switched to the next interface in the group definition
  rcv_all
    all packets from any interface are forwarded up the stack
    the IP layer will see duplicate packets

## Slide 12: broadcast/rcv_all warning
TCP will automagically remove duplicate packets
UDP will NOT
  applications based on UDP may fail or behave erratically if these QoS values are set

## Slide 13: QoS caveat
QoS modes broadcast, roundrobin, rcv_all
  not much experience in the field
  may have unexpected interactions
  recommendation is to use only online mode

## Slide 14: generating a new MAC address
Use the factory address burned into the chip
Use an address you create
  please be sure its unique
Allow the system to select an address
  00:00:A8:Index:Module Serial Number
    00:00:A8 Stratus assigned OUI
    index RNI index number 1..15
    serial num 2 bytes containing the module’s serial
    number

## Slide 15: ARP advertisements (assuming factory or user specified MAC addresses)
Early versions generated an ARP advertisement message at each switch (when needed)
1.4 does not
Use of factory setting can result in
very bad performance and or dropped
connections and or failures to connect
fxrni-389

## Slide 16: when will RNI switch
Active interface physically removed from chassis
active interface logically deleted
active interface deleted from RNI group
cable disconnected
user manually switches to another interface
and finally

## Slide 17: when will RNI switch
timeouts
  If no packets are received on the interface for a specified amount of time there is a switch
    time controlled by global value quiescent_interval
      default value is 12 seconds
    unicasts to the interface
    broadcasts
    other types of traffic are not counted

## Slide 18: when will RNI not switch
Broken device is brought back into service
interface not currently being used is removed
new interface is added
interface failure is detected but other interface is available
interface not currently being used fails

## Slide 19: probe packets
Send immediately after a switch to determine if the link is good
3 probes sent
Ethernet
  valid Ethernet V2 frame
  valid Ethernet V2 type - IP
  Not a valid IP frame
FDDI
  valid FDDI frame and LLC header
  not a valid SNAP type
Notes: Prior to RNI 1.2 the probe packet was actually pretty much a garbage packet and was sent to itself. In 1.2 it was cleaned up and was sent to 0x0000A8A8A8.

## Slide 20: Ethernet probe packets
SUMMARY Delta T Destination Source Summary
1 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
2 0.0002 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
3 0.0001 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
4 12.0010 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
5 0.0002 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
6 0.0001 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
7 12.0011 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
8 0.0002 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
9 0.0001 StrtusA8A8A8 AlBrad130FCC IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
10 12.0033 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
11 0.0002 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0
12 0.0001 StrtusA8A8A8 AlBrad130696 IP D=[0.0.0.0] S=[0.0.0.0] LEN=0 ID=0

## Slide 21: Ethernet probe packets
DLC: ----- DLC Header -----
DLC:
DLC: Frame 1 arrived at 16:04:52.5889; frame size is 178 (00B2 hex) bytes.
DLC: Destination = Station StrtusA8A8A8
DLC: Source = Station AlBrad130FCC
DLC: Ethertype = 0800 (IP)
DLC:
IP: ----- IP Header -----
IP:
IP: Version = 0, header length = 0 bytes
IP: Version number should be 4!
IP: Type of service = 00
IP: 000. .... = routine
IP: ...0 .... = normal delay
IP: .... 0... = normal throughput
IP: .... .0.. = normal reliability

## Slide 22: Ethernet probe packets
IP: Total length = 0 bytes
IP: Identification = 0
IP: Flags = 0X
IP: .0.. .... = may fragment
IP: ..0. .... = last fragment
IP: Fragment offset = 0 bytes
IP: Time to live = 0 seconds/hops
IP: Protocol = 0 (?)
IP: Header checksum = 0000, should be FFFF
IP: Source address = [0.0.0.0]
IP: Destination address = [0.0.0.0]
IP: No options
IP: [0 byte(s) of data]

## Slide 23: Ethernet probe packets
ADDR HEX ASCII
0000 00 00 A8 A8 A8 A8 00 00 BC 13 0F CC 08 00 00 00 ................
0010 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0020 00 00 52 4E 49 AD B4 9B 08 00 00 00 00 00 C6 73 ..RNI..........s
0030 2C 32 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ,2..............
0040 00 00 00 00 00 00 C6 73 2C 70 74 20 74 68 65 0A .......s,pt the.
0050 0A 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0060 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0070 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0080 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0090 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
00A0 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
00B0 00 00 ..

## Slide 24: FDDI probe packets
SUMMARY Delta T Destination Source Summary
M 1 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
2 0.00012 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
3 0.00027 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
4 11.99274 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000
5 0.00012 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000
6 0.00009 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000
7 12.00362 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
8 0.00012 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
9 0.00008 0000A8A8A8A8 CMC 0E23D3 SNAP Ethernet Type=0000
10 12.00311 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000
11 0.00010 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000
12 0.00017 0000A8A8A8A8 CMC 0E2402 SNAP Ethernet Type=0000

## Slide 25: FDDI probe packets
DLC: ----- DLC Header -----
DLC:
DLC: Frame 13 arrived at 12:28:18.74981 ; frame size is 185 (00B9 hex) bytes.
DLC: FS indicators - Error: 0, Addr recognized: 0, Frame copied: 0
DLC: FC: Asynchronous LLC Frame Priority = 0
DLC: Destination = Station 0000A8A8A8A8
DLC: Source = Station CMC 0E23D3
DLC:
LLC: ----- LLC Header -----
LLC:
LLC: DSAP Address = AA, DSAP IG Bit = 00 (Individual Address)
LLC: SSAP Address = AA, SSAP CR Bit = 00 (Command)
LLC: Unnumbered frame: UI
LLC:
SNAP: ----- SNAP Header -----
SNAP:
SNAP: Type = 0000 (Unknown)
SNAP: [164 byte(s) of data]
SNAP:

## Slide 26: FDDI probe packets
ADDR HEX ASCII
0000 50 00 00 15 15 15 15 00 00 3D 70 C4 CB AA AA 03 P........=p.....
0010 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 ................
0020 00 00 00 00 00 00 00 00 00 52 4E 49 87 00 58 00 .........RNI..X.
0030 00 04 00 E0 00 00 00 00 00 7E 3C C1 51 C6 73 2C .........~<.Q.s,
0040 70 C6 73 2C 4A 00 7B 00 7B 00 38 00 00 00 03 00 p.s,J.{.{.8.....
0050 04 00 00 20 00 20 0B 00 08 00 00 00 01 00 00 00 ... . ..........
0060 03 FF FF FF FF FF FF 08 00 FF FF FF FF FF FF 65 ...............e
0070 73 20 74 6F 74 61 6C 0A 00 00 00 00 00 00 00 00 s total.........
0080 00 00 00 00 00 00 00 00 00 00 00 00 01 08 00 06 ................
0090 04 00 01 00 00 BC 13 06 95 C6 73 2C 4A 00 00 00 ..........s,J...
00A0 00 00 00 C6 73 2C 32 00 00 00 00 00 00 00 00 00 ....s,2.........
00B0 00 00 00 00 00 00 00 00 00 .........

## Slide 27: link status
online
  manual says that the link is active only for the “active” interface
  rniadmin implies link is down
  link for all interfaces is actually up
rcv_all, broadcast, roundrobin
  manual says the links are active
  the links are really active

## Slide 28: Network Architecture requirements
All members of a group must be wired to the same subnet
they have the same IP address after all

## Slide 29: Network Architecture requirements
It is not required that each interface be connected to a separate hub
  recommended so that if a hub fails the network connect is not lost - but not required

## Slide 30: Network architecture examples
These examples use the online QoS mode
other QoS settings should be used only under special conditions

## Slide 31: Network architecture examples
simplest configuration
fault tolerance
  Stratus interfaces only

## Slide 32: Network architecture examples
fault tolerance
  Stratus interfaces
  losing hub looses only devices on that hub

## Slide 33: Network architecture examples
fault tolerance
  Stratus interfaces
Note only 1 connection between hub and switch
adding switch allows dedicated bandwidth for devices connected to switch
having hub between RNI interfaces and switch prevents the switch from seeing a topology change when RNI switches between interfaces.

## Slide 34: Network architecture examples
fault tolerance
  Stratus interfaces
2 connections directly to switch
spanning tree algorithm must be off or frames could be lost during switch
switch allows full duplex operation

## Slide 35: Network architecture examples
Fault tolerance
  Stratus interfaces
  either hub
  loosing switch only effects part of the network
spanning tree algorithm must be on
Stratus interfaces can only run in half duplex mode
  if they are the only interfaces on the hub/repeater this will not be significant

## Slide 36: Network architecture examples
Using broadcast and rcv_all QoS settings
Fault tolerance
  complete fault tolerance
  requires networks to be completely independent
  requires applications tolerate duplicate UDP packets

## Slide 37: possible gotcha’s
Jerky performance if one or more interfaces are not fully connected
  on a quiet network RNI will switch every 12 seconds to the other interface. If that interface is not connected it can be 12 seconds before there is another switch to the connected interface
  do not configure RNI on an interface that is not connected
    don’t laugh this happens a lot
    people configure it based on planned use in the future

## Slide 38: possible gotcha’s
Jerky performance if connected to a switch
  When RNI switches interfaces the switch sees a topology change and invokes the Spanning Tree Algorithm. This prevents layer 2 loops but will prevent traffic from going to or being accepted from the changed ports for some time (on the order of 10s of seconds).
  If the switch can support it and you can guarantee that layer 2 loops will not occur you can turn off the spanning tree algorithm
  use factory MAC address
    each port on switch now has a unique MAC address
    ARP advertisement is sent after RNI switches
      still may lose a packet if remote side starts sending before it gets the ARP advertisement
      ARP advertisement can get lost

## Slide 39: configuration
/etc/rni_config file
/etc/enet_config file
/etc/rc2.d/S68xrni script
/sbin/rnirc script
/sbin/rniadmin command
addrni command
rmrni command

## Slide 40: /etc/rni_config file
Defines which interfaces are part of which groups
defines the MAC address for each group
  let rni define it
  define your own
  use the burned in factory setting
Note that each non-comment line begins with #!

## Slide 41: /etc/rni_config file - example
#!rni1 enet/c6a12d0
#!rni1 enet/c4a12d0
#!rni2 enet/c6a10d0 00:11:22:33:44:55
#!rni2 enet/c4a10d0 00:11:22:33:44:55
#!rni3 enet/c2a5d0 factory
#!rni3 enet/c3a5d0 factory
Note that FDDI cards must use the factory setting

## Slide 42: /etc/enet_config file
For each network device defines its
  IP address
  subnet mask
  broadcast address
The RNI network group name corresponds to a network device

## Slide 43: /etc/enet_config file - example
#device IP address subnet broadcast
rni1 - - -
rni2 cac2 - -
rni3 cac3 - -
enet/c4a1d0 10.1.1.10 255.255.255.0 -
A dash represents a default value
  only 1 IP address can be the default. The value of ‘uname -n’ is searched for in the host file and the associated IP address is used for the interface
  subnet mask is based on the IP address
  broadcast address is based on IP address and subnetmask
    please always use the default broadcast address

## Slide 44: /etc/rc2.d/S68xrni script
Executes at run level 2
Executes before S69inetinit
  S68 forces that
For each RNI group to be setup executes the rnirc script

## Slide 45: /etc/rc2.d/S68xrni script -example
rnirc rni1
rnirc rni2
rnirc rni3

## Slide 46: /sbin/rnirc
Executes the rniadmin command on the rni group specified
  rniadmin rni1 -A
This script scould not be changed or modified in any way

## Slide 47: rniadmin usage
/sbin/rniadmin rni1 -h
rni1: ERROR: Illegal option -- h
Usage: rniadmin [ group [-A [filename]] |
[-D [filename]] |
[-a interface [address]] |
[-d member | interface] |
[-g member | interface] |
[-p member | interface [address]] |
[-q mode] |
[-s [member | interface ]] |
[-x [member | interface ]] ]

## Slide 48: rniadmin rniX -A
rniadmin [ group [-A [filename]]
  creates the RNI group specified
  adds to the group all devices associated with that group as defined in the specified file
  filename defaults to /etc/rni_config

## Slide 49: rniadmin rniX -D
rniadmin [ group [-D [filename]]
  deletes from the group all devices associated with that group as defined in the specified file
  filename defaults to /etc/rni_config

## Slide 50: rniadmin rniX -a
rniadmin [ group [-a interface [address]]
  adds to the specified RNI group the specified interface with the specified MAC address
  MAC address has the form xx:xx:xx:xx:xx:xx
  if no MAC address is given RNI will calculate one

## Slide 51: rniadmin rniX -d
rniadmin [ group [-d member | interface]
  deletes from the specified RNI group the specified interface
  interfaces can be specified by their member number or interface name
    each interface is given a member number when its added to the group based on the order in which it was added

## Slide 52: rniadmin rniX -g
rniadmin [ group [-g member | interface]
  returns the MAC address of the specified interface
/sbin/rniadmin rni1 -g 1
rni1
enet/c2a5d0 MAC address-0:0:a8:1:86:d7

## Slide 53: rniadmin rniX -p
rniadmin [ group [-g member | interface [address]]
  assigns a new MAC to the specified interface
  if no address is given RNI will calculate an address
/sbin/rniadmin rni1 -p 1 00:11:22:33:44:55
rni1
enet/c2a5d0
old MAC address-0:0:a8:1:86:d7
new MAC address-0:11:22:33:44:55
  Note that MAC address must be supplied with leading 0’s

## Slide 54: rniadmin rniX -q
rniadmin [ group [-q mode]
  assigns the group a quality of service (QoS) mode

## Slide 55: rniadmin rniX -s
rniadmin [ group [- s [member | interface ]]
  displays statistics about a group or a group member

## Slide 56: rniadmin -s command
# /sbin/rniadmin rni1 -s
rni1
Active Interface = 2
QOS type = XMT:ONLINE RCV:ONLINE
Switch Count = 43
Last Event = ADAPTOR FAILURE
Network State = UP
SAP = IP ARP
Interfaces = 2
Notes: Active interface current active interface
QoS type transmit and receive QoS settings
switch count total number of times traffic has been switch
between any of the member interfaces
last event most recent activity that caused a switch
network state state of the network
SAP service access points - IP and ARP
interfaces number of interfaces in group

## Slide 57: rniadmin -s command
#1 Interface = enet/c2a5d0 READY
Link State = DOWN
MAC Address = 0:0:a8:1:86:d7
MTU = 1497
MAC Type = 802.3 ETHERNET
Service Mode = CONNECTIONLESS
Packet Sent(err) = 0(0)
Packet Rcvd(err) = 0(0)
Packet Dropped = 0
Collisions = 0
Switch Count = 21
Notes: Interface device path and interface status
link state status of the internal connection between RNI
and lower layer drivers
not the 10BaseT link state
MAC address IEEE mac address of the interface
MTU maximum transmission unit
mac type type of interface
service mode type of communication connection
packet sent number of packets sent to the interface by RNI
packet received number of packets received by RNI from the
interface
collisions number of ethernet collisions detected by the
interface
switch count number of times RNI switched to this interface

## Slide 58: rniadmin -s command
#2 Interface = enet/c4a6d0 READY
Link State = UP
MAC Address = 0:0:a8:1:86:d7
MTU = 1497
MAC Type = 802.3 ETHERNET
Service Mode = CONNECTIONLESS
Packet Sent(err) = 188(0)
Packet Rcvd(err) = 0(0)
Packet Dropped = 0
Collisions = 0
Switch Count = 22

## Slide 59: RNI events
ACTIVE DEVICE WAS REMOVED
  interface receiving traffic was physically removed
ADAPTER FAILURE
  board no longer operational
INTERFACE FAILURE DETECTED
  problem specific to an interface was detected
NONE
  no event recorded
PROTOCOL ERROR
  RNI had a problem communicating with the interface

## Slide 60: RNI events
SWITCH ON USER REQUEST
  user manually switched via the rniadmin -x option
RECEIVE TIMEOUT
  adapter has not received any packets for quiescent_interval seconds
ROUNDROBIN SWITCHING
  roundrobin QoS is set
UNSPECIFIED REASON
  none of the above

## Slide 61: rniadmin rniX -x
rniadmin [ group [- x [member | interface ]]
  makes the specified interface the active interface
  if no interface is specified the next interface in the list is selected

## Slide 62: addrni command
Undocumented
automates most of the tasks needed to create an RNI group
can only be run from the console
# addrni
this command only valid from console terminal

## Slide 63: addrni command
# addrni
-------------------------------------------------------------------------
RNI 1.2 Setup Utility for TCP/IP.
To setup RNI, you will be asked to provide the following information:
- name of RNI device(e.g., 'rni1')
- the IP address of the RNI device (optional)
- the netmask of the IP subnet (optional)
- the network broadcast address (optional)
If any of required information is not ready, just hit <RETURN> to exit.
-------------------------------------------------------------------------
Available RNI Group Names:
rni1 rni11 rni13 rni15 rni3 rni5 rni7 rni9
rni10 rni12 rni14 rni2 rni4 rni6 rni8
Configured RNI Groups:
rni1

## Slide 64: addrni command
Enter RNI Group Name (<RETURN> if no more RNI group to define): rni2
Select interfaces to be configured under 'rni2'.
[1] c2a2d6(in use):
Modelx Description State Code Flg Serial BdRv PcRv Slotloc
- Ethernet( 10 Mbps) onln - --- - - - 2 0 2 6
Assign it to 'rni2'?[y/n] n
more interfaces to be assigned?[y/n] y
[2] c2a4d0:
Modelx Description State Code Flg Serial BdRv PcRv Slotloc
- PCI_FDDI onln - --- - - - 2 0 4 0
Assign it to 'rni2'?[y/n] y
Error 0

## Slide 65: addrni command
[3] c2a5d6:
Modelx Description State Code Flg Serial BdRv PcRv Slotloc
- Ethernet(100 Mbps) onln CABLE --- - - - 2 0 5 6
Assign it to 'rni2'?[y/n] y
[4] c3a4d0:
Modelx Description State Code Flg Serial BdRv PcRv Slotloc
- PCI_FDDI onln - --- - - - 3 0 4 0
Assign it to 'rni2'?[y/n] n
more interfaces to be assigned?[y/n] n
Total of 2 interfaces assigned to 'rni2'

## Slide 66: addrni command
Host Name (or IP Address) for rni2(default:hercules): 172.31.1.123
there is no such host in your /etc/hosts file
#ident "$Header: /p/RCS/util2/usr/src/cmd/cmd-inet/etc/hosts,v 2.3 91/09/30 12:"
(#)cmd-inet:etc/hosts 1.1"
#
# Internet host table
#
127.0.0.1 localhost
198.115.44.74 hercules
198.115.44.38 zeus
~
~
:q
Netmask for rni2(default 0xffffff00):
Broadcast Address for rni2(<RETURN> for default):
Oct 25 13:50:26.46 [RNI 17,cpu0] rni2: interface enet/c2a5d6 network connectiont

## Slide 67: addrni command
Available RNI Group Names:
rni1 rni11 rni13 rni15 rni3 rni5 rni7 rni9
rni10 rni12 rni14 rni2 rni4 rni6 rni8
Configured RNI Groups:
rni1
rni2
Enter RNI Group Name (<RETURN> if no more RNI group to define):
#

## Slide 68: addrni command
#tail rni_config
#!rni1 enet/c2a2d7 factory
#!rni1 enet/c2a5d7 factory
#!rni2 enet/c2a4d0
#!rni2 enet/c2a5d6
# tail enet_config
enet/c2a2d6 - 255.255.255.0 -
rni1 10.1.1.20 - -
rni2 172.31.1.123 0xffffff00 -
# cat S68xrni
echo waiting for RNI devices to be online...
rnirc rni1
rnirc rni2

## Slide 69: addrni command
What do you need to do?
#rnirc rni2
# /etc/rc2.d/S69inetinit inetstart rni2
/etc/rc2.d/S69inetinit: Defining host name as 172.31.1.123 for rni2

## Slide 70: rmrni
Undocumented
automates most of the tasks needed to remove an RNI group
can be run from any terminal

## Slide 71: rmrni
Before removing an RNI group stop it with
# /etc/rc2.d/S69inetinit stop rni2

## Slide 72: rmrni
# rmrni
You have:
rni1
rni2
remove rni1?(y,n,q): n
remove rni2?(y,n,q): y

## Slide 73: rmrni
# tail /etc/rni_config
#!rni1 enet/c2a2d7 factory
#!rni1 enet/c2a5d7 factory
# tail /etc/enet_config
enet/c2a2d6 - 255.255.255.0 -
rni1 10.1.1.20 - -
# cat /etc/rc2.d/S68xrni
echo waiting for RNI devices to be online...
rnirc rni1

## Slide 74: RNI anomalous event messages
If the network is running, no action is required. If the
condition continues, contact the system administrator.
%s UDERR %s dl_err 0x%x
  An error acknowledge was returned with the indicated error status on a UDP request.
?BIND_=0x%x,state=%d) <--- 0x%x
  A BIND request returned the indicated REQ rror(errno=0x%x,unix_errno error status.
%s: failed switching to %s, error (0x%x, 0x%x)
  A BIND request returned the indicated error status.

## Slide 75: RNI anomalous event messages
?%s unexpected event detected 0x%x
  The RNI driver received an unsolicited error indication with an unrecognized event code.
?UNBIND_REQ error(errno=0x%x,unix_errno=0x%x,state=%d) <--- 0x%x
  An UNBIND request returned the indicated error status.
"?%s cmd (0x%x) failed on %s (0x%x,0x%x,%d,0x%x)"
  An error acknowledgement message was received.
%s interface %s output queue full
  The indicated device and interface have a full output queue.

## Slide 76: RNI interface switch messages
no action is required.
%s: switched from %s to %s (INTERFACE OFFLINE)
  The indicated Stream was switched from its original interface to a back-up interface because the original interface was taken offline.
%s: switched from %s to %s (CABLE DISCONNECT)
  The indicated Stream was switched from its original interface to a back-up interface because the original interface's cable was disconnected.
%s: switched from %s to %s (LLC ERROR)
  The indicated Stream was switched from its original interface to a back-up interface because the original interface experienced link level protocol errors.

## Slide 77: RNI interface switch messages
%s: switched from %s to %s (USER REQUEST)
  The indicated Stream was switched from its original interface to a back-up interface at the request of the Stream user.
%s: switched from %s to %s (INTERFACE DELETED)
  The indicated Stream was switched from its original interface to a back-up interface because the original interface was deleted.
%s: switched from %s to %s (OUTPUT QUEUE FULL)
  The indicated Stream was switched from its original interface to a back-up interface because the original interface's output queue was full.

## Slide 78: RNI network connection messages
%s: interface %s network connection lost
  The indicated Stream lost its network connection.
  Action: Reseat cable connectors. If the condition persists, run diagnostics to identify the problem.
%s: interface %s network connection restored
  The indicated STREAMS network connection was restored.

## Slide 79: RNI streams message
%s detects %s (state %d)is not totally controlled by RNI, please stop the network
  The indicated STREAMS network connection is in an anomalous state.
  Action: Shut down the network, and restart.

## Slide 80: example console messages
cable pulled from c2a2d7
Oct 26 17:12:09.51 [RNI 17,cpu1] rni1: interface enet/c2a2d7 network connection lost
Oct 26 17:12:09.51 [RNI 12,cpu1] rni1: switched from enet/c2a2d7 to enet/c2a5d7
(CABLE DISCONNECT)
cable inserted
Oct 26 17:12:16.94 [RNI 18,cpu0] rni1: interface enet/c2a2d7 network connection
restored
manually switch (rniadmin -x)
Oct 26 17:16:25.93 [RNI 14,cpu1] rni1: switched from enet/c2a2d7 to enet/c2a5d7 (USER REQUEST)
Notes: Messages are displayed immediately when cable is pulled or inserted

## Slide 81: example elgpost messages
cable pulled from c2a2d7
Oct 26 17:12:09.51 [RNI:I RNI_CABLE_CUT ,cpu1] rni1: interface enet/c2a2d7 network connection lost
Oct 26 17:12:09.51 [RNI:I RNI_SWITCH_NET_DISC ,cpu1] rni1: switched from enet/c2a2d7 to enet/c2a5d7 (CABLE DISCONNECT)
cable inserted
Oct 26 17:12:16.94 [RNI:I RNI_CABLE_RESTORED ,cpu0] rni1: interface enet/c2a2d7 network connection restored
manually switch (rniadmin -x)
Oct 26 17:16:25.93 [RNI:I RNI_SWITCH_X_REQ ,cpu1] rni1: switched from enet/c2a2d7 to enet/c2a5d7 (USER REQUEST)

## Slide 82: debugging
If running at 100 mbps try 10
  cat 5 cable, connection or installation may be substandard
If running full duplex, try half duplex
  if its not a K460 if MUST be half duplex
If running on a K104 make sure transceiver has SQE turned on
Delete all interfaces but 1
  deal with only 1 interface at a time

## Slide 83
debugging When at the end of your rope
Call the CAC