## Slide 1: Your Application from the Network’s Perspective
Noah Davids
Software Systems Engineer
Notes: Rev 2 02-09-04
Rev 3 02-09-06 (updated to conform to review comments)
Rev 4 02-09-09 (added trademark slide)
presented at Stratagy 2002
October 20-23, 2002
San Antonio, TX
Session T15303

## Slide 2: Introduction
The network sees your application as a sequence of
  Frames at layer 2
  Packets at layer 3
  Segments at layer 4
Your application’s frames and packets may go through several different networks at layer 2 and 3

## Slide 3: Introduction
Understanding how sequences of frame/packet/segments and your networks interact can be the difference between an application design that works satisfactorily in the production environment instead of just the test environment
  Or in several different production environments

## Slide 4
Background

## Slide 5: Delay versus Throughput
Delay
  End to end time to transmit a single packet
Throughput
  Long term rate of transmission

## Slide 6: Types of delays
Insertion delay
  Time to write the packet onto the communications link
Propagation delay
  Time for the frame to travel down the communications link
    Physical distance and network components

## Slide 7: Types of delays
Processing Delay
  Time for a hub/switch/router/thingy to process the packet
Queuing Delay
  Time that a packet is waiting in a buffer before being acted on, I.e. processed or transmitted

## Slide 8: Insertion Delays
Time between the transmission of the first bit of the packet to the time of transmission of the last bit of the packet
  T = 8 * size in bytes / line speed in bits per sec
  include all protocol overhead bytes

## Slide 9: Insertion Delays (in milliseconds)
Protocol Minimum Maximum
46 data bytes (with overhead) 1500 data bytes
Ethernet 0.0576 (72) 1.2208 (1526)
Fast Ethernet 0.0057 (72) 0.1220 (1526)
Gigabit Ethernet 0.0005 (72) 0.0122 (1526)
T1 (ATM) 0.5492 (106) 8.7875 (1696)
T3 (ATM) 0.0189 (106) 0.3032 (1696)
T1 (Frame Relay) 0.2694 (52) 7.8031 (1506)
T3 (Frame Relay) 0.0092 (52) 0.2693 (1506)
Notes: Ethernet overhead
preamble (8), destination (6), source (6), type/length (2), CRC (4)
ATM
5 bytes header, 48 bytes data per cell
Frame Relay
flag (1), DLCI (2), CRC (2), flag (1)
T1 = 1.544 mbps
T3 = 44.736 mbps

## Slide 10: Propagation Delays
Speed of light in a vacuum
  5.35 milliseconds / 1000 miles
UTP (unshielded twisted pair)
  177,000 km/sec
  0.565 microseconds / 100 meters

## Slide 11: Propagation Delays
Typical terrestrial facilities (including microwave, coax, and fiber)
  8 milliseconds / 1000 miles
  Don’t use a map
    Route from Phoenix to New York may go thru LA, Denver, Dallas and Chicago, find actual length from carrier
Geosynchronous satellite facilities (transponder to transponder)
  Add 280 milliseconds to rest of link

## Slide 12: Processing Delays
Early X.25 switches 20 – 100 msec
Modern IP routers performing fast path routing less than 1 milliseconds
  8 milliseconds / 1000 miles has this factored in.
I’ll ignore processing delays from now on

## Slide 13: Queuing Delays
This slide inserted for completeness
I’m not even going to try to talk about queuing theory

## Slide 14: Bandwidth Delay Product
bandwidth delay product =
bandwidth * delay
  Bandwidth is the minimum bandwidth of the end to end connection
  Delay includes all delays from end to end
    Ping times are a fair estimate

## Slide 15
Layer 2
Ethernet

## Slide 16: Reference Network 1 (RN-1)
Single LAN segment
Shared media

## Slide 17: Layer 2 – Ethernet
A stream of frames
  No relationship between one frame and the next
Insertion delays in milliseconds (including 8 byte preamble)
  Ethernet 0.0576 (72) 1.2208 (1526)
  Fast Ethernet 0.0057 (72) 0.1220 (1526)
  Gigabit Ethernet 0.0005 (72) 0.0122 (1526)
Interframe Gap (IFG)
  9.6/0.96/0.096 microseconds in Ethernet/Fast/Giga
No significant propagation delays

## Slide 18: Layer 2 – Ethernet Collisions
Collisions are not a significant issue until you start getting a lot of them on the same frame
  Even then it is not that big a deal
  30% collisions is a myth

## Slide 19: Layer 2 – Ethernet Late Collisions
Don’t confuse collisions with late collisions
  Late collisions are not retransmitted by the chip
  Typically indicates a network operational or design problem
    Full duplex/half duplex mismatch
    Cables too long
    Chip failing

## Slide 20: Layer 2 – Ethernet Excessive Collisions
Don’t confuse collisions with excessive collisions
  After 16 tries the chip gives up and drops the frame
  Typically indicates an overloaded network or an operational problem
    Badly overloaded switch with backpressure
      You will see a great many more deferrals than collisions
    Chip failing
    Full duplex/half duplex mismatch

## Slide 21: Layer 2 – Ethernet Collisions
Notes: Note that the first row represents a 100% collision rate, I.e. every frame generates 1 collision.
This is for a 10 meg network
The 0 column is the time needed to wait for a frame to be transmitted from another station, in this case none.
Table from “when packets collide” SysAdmin magazine June 1998
http://www.samag.com

## Slide 22: Layer 2 – Ethernet Deferrals
A deferral occurs when an Ethernet chip goes to transmit a frame and finds the communication media already in use.
  An Ethernet chip will always try to transmit 9.6 microseconds (10 mbps) (IFG) after the previous transmission ends
  If 2 stations have deferred they are guaranteed to collide

## Slide 23: Layer 2 – Ethernet Deferrals
Assume that just as the Ethernet chip is about to transmit the first bit of another frame is seen
If that frame is maximum length it will be 1.2304 milliseconds (10 mbps) before it can start and 2.4512 milliseconds before it can finish (assuming it is also a max frame)
  To start
    Max insertion delay + 9.6 microseconds IFG
  To finish
    Plus another max insertion delay

## Slide 24: Layer 2 – Ethernet Deferrals
If each frame in a 5 meg file transfer has to defer to 1 maximum frame from another station (100% deferral rate)
  5 meg file = 3,591 max frames + 1 shorter
  3592 * 1.2304 = 4.4183 seconds
    Additional time – with no collisions

## Slide 25: Reference Network 2 (RN-2)
Single LAN segment
Switched network

## Slide 26: Layer 2 – Ethernet switched - store and forward
Entire frame is read and stored and checked for errors before it is transmitted out destination port
Latency is typically much much higher for store and forward switches then for cut through switches

## Slide 27: Layer 2 – Ethernet switched - cut through
As soon as destination address is read the frame is redirected
  Early frame bits are transmitted while later ones are still being read
Errored frames are forwarded to destination
Latency is typically 40 microseconds (10 mbps), if destination port is free
  If destination port is not free latency will depend on queuing time for the port

## Slide 28: Layer 2 – Ethernet switched - backpressure
Some switches will generate a collision when they are overloaded in order to force the transmitter to stop
  Lots more single and multiple collisions than deferrals
Overload may be overall volume that the switch is handling or overload on 1 or a few destination ports
Switch may also be dropping packets
This should be investigated and the switch probably upgraded

## Slide 29: Layer 2 – Ethernet switched – full duplex
Switched networks can run as full duplex
  No collisions
  No deferrals
    This is the more significant from a performance point of view
  Flow control handled by 802.3x
    May result in dropped frames if flow control is not supported by both hosts
    Layer 2 flow control can screw up TCP congestion control and avoidance algorithms.

## Slide 30: Layer 2 – Ethernet switched – full duplex
Significant errors unless both stations (host and switch port) configured as full duplex
  CRC and alignment errors
  Excessive and late collisions

## Slide 31: Layer 2 – Ethernet summary
Nothing you can do at the application programming level
At the network operations level
  Ignore “normal” collisions
    But remember that late and excessive collisions are significant
  Deferrals can add significant amount of time to the insertion delay
    High deferral rates probably indicate an overloaded network

## Slide 32: Layer 2 – Ethernet summary
Investigate if a switch appears to be using backpressure or flow control
Beware of CRC, alignment or other errors
  10BaseT spec 1 error bit per 109 (1 billion) bits
    1 error in 81,914 maximum sized frames (1,518 bytes + 8 byte preamble)
    1 error in 473,485 small frames (256 bytes + pre)
    1 error per 100,000 frames probably something to worry about
  100BaseT spec: 1 error bit per 1012 bits

## Slide 33
Layer 3
IP

## Slide 34: Reference Network 3 (RN-3)
Multiple RN-1s or RN-2s
Connected via router and LAN links

## Slide 35: Reference Network 4 (RN-4)
Multiple RN-1s or RN2-s
Separated by slow or long links

## Slide 36: Reference Network 5 (RN-5)
Multiple RN-1s or RN-2s
Separated by fast (T1 or T3) or short links

## Slide 37: Layer 3 – IP
A stream of packets
  no relationship between one packet and the next
    Except for fragmentation
Don’t forget all the Layer 2 issues
  Remember that each frame is inserted multiple times, once by the sender and once by each router

## Slide 38: Layer 3 – IP Fragmentation
Each network layer has a maximum transmission unit (MTU)
If a packet is larger than the MTU the router must fragment it
This slows down the router
  Packets requiring fragmentation take a much slower path through the router
The probability that the packet will be lost goes up proportional to the number of fragments

## Slide 39: Layer 3 – IP Fragmentation
Typically more of an issue when the router is connecting WAN links then when it is connecting Ethernet
Most TCP stacks will user small packets (maximum segment size (MSS)) when the packets are being routed
  OS_TCP 512 bytes (otp-868)
  STCP 536 bytes
  Windows® 2000 dynamic 536 bytes
  HP-UX® dynamic 536 bytes
Notes: otp-868 will change it to 536

## Slide 40: Layer 3 – IP Fragmentation
To increase default MSS to 1460
  OS_TCP
    as: set_longword tcpos_default_mss$ 5b4
  STCP
    as: set_longword default_min_mtu 5c8
  HP-UX
    Dynamic determination
    ndd –h ip_pmtu_strategy
  Windows 2000
    Dynamic determination for a connection is default
      Set to 0 to use 536 without trying discovery
      HKEY_LOCAL_MACHINE\SYSTEM\
      CurrentControlSet\Services\Tcpip\Parameters\
      EnablePMTUDiscovery

## Slide 41: Layer 3 – IP Fragmentation
UDP
  There is nothing in the UDP stack to adjust packet size based on local or remote networks
  If you send more than the MTU of the network it will cause fragmentation
    Typically 1472 bytes (1500 – IP + UDP headers)

## Slide 42: Layer 3 – IP Fragmentation
Check the selected MSS for fragmentation at the remote end
  Count fragmented packets with netstat
  Use a protocol analyzer and look at the packets for fragmentation
Remember
  network paths may change and what doesn’t cause fragmentation today may tomorrow
  Check paths to all destinations – what is good for 1 destination may hurt another

## Slide 43: Layer 3 – IP summary
Avoid fragmentation
  Check receiving host netstat statistics for “fragments received”
At the application layer
  Avoid sending UDP packets larger than the minimum MTU
At the network operations layer
  Make sure that the TCP MSS is not adjusted to adversely effect some networks (or at least make a conscious decision to do this)

## Slide 44
Layer 4
TCP

## Slide 45: Layer 4 – TCP
Sequence of related segments
How client and server applications interact can have a profound impact on performance

## Slide 46: Layer 4 TCP Types of sequences
Ping pong
  Side “A” sends a segment, wait for a response from side “B”, side “A” sends another segment waits for a response from side “B”
    telnet, DNS query, NFS, TFTP
Pinball
  Side “A” sends a segment, get back lots of segments from side “B”, side “A”sends another segment, get back even more segments from side “B”
    Web browsing, FTP

## Slide 47: Layer 4 TCP Types of sequences
Ping-ball
  Sometimes acts like ping pong sometimes like pinball

## Slide 48: Layer 4 TCP ping-pong sequences
Side “A” sends a segment, wait for a response from side “B”, side “A” sends another segment waits for a response from side “B”
  telnet, DNS query, NFS, TFTP

## Slide 49: Layer 4 TCP ping-pong sequences
Overall delay is
  (“A+B” insertion delays + propagation delay) * volley length
The longer the volley the more pronounced the effect
The slower the network the more pronounced the effect

## Slide 50: Layer 4 TCP ping-pong sequences RN-1
Notes: 10 meg Ethernet – time is in seconds

## Slide 51: Layer 4 TCP ping-pong sequences RN-4
Notes: 10 meg Ethernet to 1000 miles Frame Relay over 64K to 10 me Ethernet – time is in seconds

## Slide 52: Layer 4 TCP ping-pong sequences RN-5
Notes: 10 meg Ethernet to 1000 miles Frame Relay over T1 to 10 meg Ethernet – time is in seconds

## Slide 53: Layer 4 TCP ping-pong sequences - summary
Ping pong sequences don’t work well over large delay networks
  Combine data to reduce number of segments/volleys
  Adjusting TCP window sizes won’t help
  Adjusting MSS may help (but avoid fragmentation)
Lost segments will significantly increase delay
  Retransmission must wait for retransmission timer to expire

## Slide 54: Layer 4 TCP pinball sequences
Side “A” sends a segment, get back lots of segments from side “B”, side “A”sends another segment, get back even more segment from side “B”
  Web browsing, FTP

## Slide 55: Layer 4 TCP pinball sequences
Delay is not significant, throughput is
Throughput is controlled by
  TCP congestion window size
  TCP send window size
  TCP receive window size

## Slide 56: Layer 4 TCP TCP congestion window
Controls how many segments can be outstanding (not ACKed) at any given time
TCP Slow Start
  Congestions window starts with 1 segment
  Every successful ACK adds 1 more segment until congestions window = receive window
  Results in exponential increase in cwnd
    1, 2, 4, 8, …

## Slide 57: Layer 4 TCP TCP congestion window
Congestion avoidance
  If the retransmission timer goes off or a duplicate ACK is received
    ssthresh = max (2, (min (cwnd, receive window)/2)
  If retransmission times goes off
    cwnd = 1
  When ACK for new data is received
    If (cwnd <= ssthresh)
      cwnd++
      else
      cwnd = segment size * segment size /cwnd + cwnd
  Results in linear growth until cwnd = ssthresh then exponential

## Slide 58: Layer 4 TCP TCP send window
Controls how many bytes can be buffered by the sender and therefore how many unACKed segments can be outstanding
Also controls how many bytes can be buffered after the receive window closes

## Slide 59: Layer 4 TCP TCP send window
In OS_TCP, FTX™, HP-UX, Windows 2000 controlled by the sender with a socket option SO_SNDBUF
STCP doesn’t support SO_SNDBUF

## Slide 60: Layer 4 TCP TCP send window
send window sizes (in bytes)
  default maximum
  Windows 2000 ? ?
  OS_TCP 11,468 32,768
  STCP 11,588 32,768
    will change based on connection
  HP-UX 11 32,767 262,142
    65535 for fast links
    8192 for slow links

## Slide 61: Layer 4 TCP TCP receive window
Controls how many bytes can be buffered by the receiver in the TCP stack
  The current window is advertised in each TCP header as the “window”.
  If an application fails to read data, TCP will still ACK it and will advertise a reduced window in the header of the ACK segment
  If a zero window is advertised the sender must stop sending data
    Although it is allowed to send window probes to make sure that an increase in the window has not been missed.

## Slide 62: Layer 4 TCP TCP receive window
Controls how many bytes can be sent by the sender before waiting for an ACK
  The sender can send up to the advertised receive window without waiting for an ACK
In OS_TCP, FTX, HP-UX, Windows 2000 controlled by the receiver with the socket option SO_RCVBUF
STCP doesn’t support SO_RCVBUF but dynamically increases the window if it sees that the connection is a “receive only”

## Slide 63: Layer 4 TCP TCP receive window
receive window sizes (in bytes)
  Default Maximum
  Windows 2000 17,520 1,073,741,823
    It is somewhat dynamic based on the MSS
  OS_TCP 11,468 32,768
  STCP 8,192 65,535
    will change based on connection
  HP-UX 11 32,767 262,142
    65535 for fast links
    8192 for slow links

## Slide 64: Layer 4 TCP TCP window sizes
Optimal window size
  Bandwidth delay product rounded up to the next segment size
  To handle error recovery send window should be 2 or even 3 times bandwidth delay product
    At least according to some sources

## Slide 65: Layer 4 TCP TCP window sizes
Cross county (5000 miles) on a 64KB line
  insertion delay = 0.079 sec
  536 + 48 (data + overhead) * 8 / 64,000
  48 (ack) * 8 / 64,000
  propagation = .040 sec
  5000 miles * 8 ms / 1000 miles
  processing delay (at host) = 0.002 sec (local ping)
Slowest link speed * round trip delay
  (0.079 + 0.040 + 0.002) * 64,000 = 7,744 bits
  7,744 / 8 = 968 bytes
  Buffer size = 1072 (2 * 536)

## Slide 66: Layer 4 TCP TCP window sizes
Cross county (5000 miles) on a T1 line
  insertion delay = 0.003 sec
  536 + 48 (data + overhead) * 8 / 1,540,000
  48 (ack) * 8 / 1,540,000
  propagation = .040 sec
  5000 miles * 8 ms / 1000 miles
  processing delay (at host) = 0.002 sec (local ping)
Slowest link speed * round trip delay
  (0.003 + 0.040 + 0.002) * 1,540,000 = 69,300 bits
  69,300 / 8 = 8,663 bytes
  Buffer size = 9,112 (17 * 536)

## Slide 67: Layer 4 TCP TCP window sizes
Cross county (5000 miles) on a T3 line
  insertion delay = 0.0001 sec
  536 + 48 (data + overhead) * 8 / 44,736,000
  48 (ack) * 8 / 44,736,000
  propagation = .040 sec
  5000 miles * 8 ms / 1000 miles
  processing delay (at host) = 0.002 sec (local ping)
Slowest link speed * round trip delay
  (0.0001 + 0.040 + 0.002) * 44,736,000 = 1,883,385 bits
  1,883,385 / 8 = 235,423 bytes
  Buffer size = 235,840 (440 * 536)

## Slide 68: Layer 4 TCP TCP window sizes
100 mbps local LAN
  insertion delay = 0.0001274 sec
  0.1220 ms for max data segment
  0.0054 ms for ack
  propagation = 0.00000113 sec
  .565 microseconds / 100 meters
  processing delay (at host) = 0.002 sec (local ping)
Slowest link speed * round trip delay
  (0.002) * 100,000,000 = 200,000 bits
  200,000 / 8 = 25,000 bytes
  Buffer size = 26,280 (18 * 1460)

## Slide 69: Layer 4 TCP TCP window sizes
1000 mbps local LAN
  insertion delay = 0.00001227 sec
  0.0122 ms for max data segment
  0.0005 ms for ack
  propagation = 0.00000113 sec
  .565 microseconds / 100 meters
  processing delay (at host) = 0.002 sec (local ping)
Slowest link speed * round trip delay
  (0.002) * 1,000,000,000 = 2,000,000 bits
  2,000,000 / 8 = 250,000 bytes
  Buffer size = 251,120 (172 * 1460)

## Slide 70: Layer 4 TCP TCP window sizes
Speed | Distance | Buffer size
64KB | 5000 miles | 1,072
T1 | 5000 miles | 9,112
T3 | 5000 miles | 235,840
Fast Ethernet | local | 26,280
Gigabit Ethernet | local | 251,120

## Slide 71: Layer 4 TCP summary
The number of unACKed segments that can be outstanding at any one time is the minimum of the
  Congestion window
  Send window
  Receive window
It may not be possible to set an optimal window but get as close as possible

## Slide 72: Layer 4 TCP summary
lost segments totally destroy throughput
  Reduced congestion window
  Retransmission timeouts
    See Spring 2001 Stratasphere “Packet Loss” for complete details
If the send or receive windows are too small the sender must stop and wait for ACKs to be received
  This significantly reduces throughput

## Slide 73: Layer 4 TCP summary
Optimal window size is primarily a function of
  Propagation delay for WANs
  Processing delay for LANs

## Slide 74
Unanticipated conversion from Pinball
to
ping pong

## Slide 75: Nagel Algorithm
Only 1 packet < MSS can be outstanding at any one time
Once the first small packet is sent data is buffered until it equals MSS or the ACK is received

## Slide 76: Nagel Algorithm
MSS = 1460
Send 100 bytes followed by 5000 bytes
  Segment 1 = 100 bytes
  Segments 2, 3, 4 = 4,380 bytes
  Segment 5 = 620 bytes will not be sent until the ACK from segment 1 is received

## Slide 77: Nagel Algorithm
Solution #1
  Turn off Nagel with the NODELAY socket option
Solution #2 (better)
  Control writes so that small segments are not sent before large ones

## Slide 78: Delayed ACK
TCP will delay sending an ACK for a given period of time
This allows time for the application to send a reply and the ACK can be piggy backed on that data
  Reduces number of packets and packet overhead
Coupled with Nagel this can significantly reduce throughput

## Slide 79: Delayed ACK
Delayed ACK timer
  OS_TCP 200 ms
    Patchable but strongly recommend that it be left as is
      It effects other things besides the delayed ACKs
  STCP 200 ms
    Not patchable
  HP-UX 11 50 ms
    Changes are not supported
  Windows 2000 200 ms
    Registry value is TcpDelAckTicks

## Slide 80: Delayed ACK
Solution #1
  Turn off Nagel
Solution #2 (better)
  Have the receiver send a reply when data is read
    Increases overhead but allows sender to confirm receipt of data
      Sender doesn’t have to wait for reply (not suggesting ping-pong)
        reads and writes done asynchronously

## Slide 81: TCP Slow Start Congestion Avoidance
Application cannot control this
Network should be error/congestion free
  Dropped packets trigger congestion avoidance which slows throughput down on purpose by requiring more ACKs

## Slide 82: 0 Receive Window
Receiver is not reading data fast enough so that the receiver’s TCP buffer fills and it advertises a 0 window
Bandwidth delay is large enough or receive window is small enough so that the entire window can be filled before it is possible for sender to get an ACK

## Slide 83: 0 receive window receiver not reading fast enough
Receiver advertises 0 window
Sender stops
Receiver reads 1 or 2 segments
  sends a new window advertisement
Sender sends 1 or 2 segments
  and must stop again until it gets another window advertisement
The net effect is as if the receiver window is only 1 or 2 segments – at least until the receiver can catch up and empty the receive queue.

## Slide 84: 0 receive window large bandwidth delay with too small receive window
Default OS_TCP receive window = 11,468
  Over a T3 can be transmitted in
    11,468 / 536 = 21.3
    (22 * 48 + 11,468) * 8 / 44,736,000
    0.00223 seconds
  If RTT is 8 ms we will have to wait over 5ms before we can send again
    Reducing throughput by 72%
      (22 * 48 + 11,468) * 8 / 0.008 = 12,524,000
      (44,736,000 – 12,524,000) / 44,736,000 * 100
      72%

## Slide 85: Summary
Existing applications
  Understand the pattern of F/P/S
  Before moving the application onto a new network understand the network
    This includes
      moving the application to a different server on a different network
      Adding or changing clients so that they are using a different network

## Slide 86: Summary
New applications
  Understand the network that the application will run on
  Code so that the pattern of F/P/S works well in that environment
    If possible code that it will work well in any environment

## Slide 87
References
Internetworking with TCP/IP volumes 1, 2, 3
  Douglas E Comer
Internet Core Protocols
  Eric Hall
Enhancing LAN Performance
  Gilbert Held
Wide-Area Data Network Performance Engineering
  Robert G. Cole and Ravi Ramaswamy

## Slide 88
References
http://standards.ieee.org/regauth/oui/index.shtml
  List of public OUIs
http://www.rfc-editor.org/rfc.html
  Official RFC database (identifies obsolete RFCs)
http://www.iana.org/
  Internet assigned numbers authority
http://www.protocols.com/pbook/
  RADCom Protocol Directory
http://www.private.org.il/tcpip_rl.html
  General TCP/IP resource/reference list

## Slide 89: Questions
-1 = -1
-1 / 1 = 1 / -1
SQRT (-1 / 1) = SQRT (1 / -1)
SQRT (-1) / SQRT(1) = SQRT (1) / SQRT (-1)
i / 1 = 1 / i
i / 2 = 1 / (2i)
i / 2 + 3 / (2i) = 1 / (2i) + 3 / (2i)
i (i / 2 + 3 / (2i) ) = i ( 1 / (2i) + 3 / (2i) )
(i2) / 2 + (3i) / 2i = i / (2i) + (3i) / (2i)
(-1) / 2 + 3 / 2 = 1 / 2 + 3 / 2
1=2

## Slide 90
Trademark Information
Stratus, the Stratus logo, ftServer, Continuum,
Continuous Processing, StrataLINK, and StrataNET are registered trademarks; the Stratus Technologies logo, the ftServer logo, the Stratus 24 x 7 logo, the Continuum logo, The World’s Most Reliable Servers, The World’s Most Reliable Server Technologies, ftMessaging, ftStorage, and ftMemory are trademarks and ftService is a service mark of Stratus Technologies Bermuda Ltd.
All other trademarks are the property of their respective owners.
Specifications and descriptions are summary in nature and subject to change without notice.
© 2002 Stratus Technologies Bermuda Ltd.